S-57 APPENDIX B.1
Annex A - Use of the Object Catalogue for ENC

This document must only be used with Edition 2.0 of the / ENC Product Specification - S-57 Appendix B.1

S-57 Appendix B.1 - Annex A	April 2002	Edition 2.1

Page intentionally left blank

CONTENTS

Figures

Page intentionally left blank

# 1. Introduction

## 1.1 General

The following clauses specify the conventions that must be used to encode the geometry and semantic description of each object in an ENC. This document is laid out, as far as possible, along the lines of the IHO publication “Chart Specifications of the IHO - M4".

This document describes how to encode information that the cartographer considers relevant to an ENC. The content of an ENC is at the discretion of the producing authority provided that the conventions described within this document are followed. A “producing authority” is a Hydrographic Office (HO) or an organisation authorised by a government, HO or other relevant government institution to produce ENCs.

This document is intended for use with Edition 2.0 of the ENC Product Specification (S-57 Appendix B1, Annex A) contained within S-57 Edition 3.1 which was issued in November 2000.

For details of the use of this document by producing authorities still producing ENCs conforming to S-57 Edition 3.0, see the Introduction to the Explanatory Booklet which was issued with S-57 Edition 3.1.

## 1.2 Presentation of the document

The following conventions are used:

Presentation conventions:	Object class:	WRECKS
Attribute:	EXPSOU
Mandatory attribute:	WATLEV
Prohibited attribute:	VERDAT
Attribute value:	-2.4
- Attributes_A: For each object class, the whole list of subset A is given, with the specific applicable attribute values, where required, for the feature object. Reference should be made to S-57 Annex B, Appendix B1; ENC Product Specification, section 3.5.2, for conditional mandatory attributes.
- Attributes_B, attributes_C: Except for attributes INFORM, NINFOM, and more rarely SORDAT, the attributes from subsets B and C are not mentioned in the following lists; however, this does not mean that their use is prohibited.

For definitions of attribute subsets A, B and C, see Appendix A, Chapter 1, section 1.1.

## 1.3 Use of language

Within this document:
“Must” indicates a mandatory requirement.
“Should” indicates an optional requirement, that is the recommended process to be followed, but is not mandatory.
“May” means “allowed to” or “could possibly”, and is not mandatory.

# 2. General rules

## 2.1 Cartographic framework

### 2.1.1 Horizontal datum

The horizontal datum must be unique in a data set and must be WGS 84. It must be encoded in the “Horizontal Geodetic Datum” [HDAT] subfield of the “Data Set Parameter” [DSPM] field.

The use of the meta object M_HDAT is prohibited.

The use of the attribute HORDAT on any spatial object is prohibited.

The meta object M_HOPA may be used to provide the shift from another horizontal datum to WGS 84 (see ENC Product Specification clause 4.1).

Meta object:	Horizontal Datum (M_HOPA)
Attributes:	HORDAT	to contain the original horizontal datum of the data.
SHIPAM	INFORM	NINFOM

Where data has been transformed to WGS 84 from another datum, the producing authority may wish to indicate the accuracy of the transformation. If so, it must be done using the attribute INFORM on the meta object M_QUAL.

### 2.1.2 Vertical datum

Vertical datum information is encoded using the subfield VDAT, the meta object M_VDAT, or the attribute VERDAT on individual objects. The values encoded in the attributes ELEVAT, HEIGHT, VERCCL, VERCLR, VERCOP and VERCSA are referenced to the specified datum(s). VERDAT must not be encoded on an object unless at least one of the above attributes is also encoded on that object.

The default value for the entire data set must be given in the “Vertical Datum” [VDAT] subfield of the “Data Set Parameter” [DSPM] field.

If the vertical datum for an area is different to the value given in the VDAT subfield for the data set, it must be encoded using M_VDAT. The areas covered by these meta objects must not overlap.

Meta object:	Vertical datum (M_VDAT)
Attributes:	VERDAT	INFORM	NINFOM

Height contours, going across areas having different values of vertical datum, must be split at the border of these areas.

Various datums are used on paper charts and these datums are used in the same way for ENC. For example, different datums may be used for the following:

- altitude of spot heights, height contours, landmarks,
- elevation of lights,
- vertical clearance.

Where different vertical datums are used for the various vertical measurements, the default value given by the VDAT subfield or M_VDAT applies to the first group of the above list. The attribute VERDAT on an individual object applies to the elevation of lights and vertical clearances and must only be populated if different to the value given by VDAT or M_VDAT.

### 2.1.3 Sounding datum

Sounding datum information is encoded using the subfield SDAT or the meta object M_SDAT, and must be constant over large areas. The values encoded in the attributes VALSOU, DRVAL1, DRVAL2 and VALDCO, and the sounding values encoded in SOUNDG objects, are referenced to this datum.

The default value for the entire data set must be given in the “Sounding Datum” [SDAT] subfield of the “Data Set Parameter” [DSPM] field.

If the sounding datum for an area is different to the value given in the SDAT subfield for the data set, it must be encoded using M_SDAT. The areas covered by these meta objects must not overlap.

Meta object:	Sounding datum (M_SDAT)
Attributes:	VERDAT	INFORM	NINFOM

The use of the attribute VERDAT on individual objects related to depth (e.g. DEPARE, DEPCNT, DRGARE, OBSTRN, SOUNDG, UWTROC, WRECKS) is prohibited.

Depth contours and depth areas going across areas having different values of sounding datum must be split at the border of those areas.

### 2.1.4 Units

The depth, height and positional accuracy units in a data set must be metres. They must be given in the “Units of Depth Measurement” [DUNI], “Units of Height Measurement” [HUNI] and “Units of Positional Accuracy” [PUNI] subfields of the “Data Set Parameter” [DSPM] field.

The use of the meta object M_UNIT is prohibited.

### 2.1.5 Dates

When encoding dates using the attributes CPDATE, DATEND, DATSTA, PEREND, PERSTA, SORDAT, SUREND and SURSTA, and no specific year, month or day is required, the following values must apply in conformance to ISO 8601:1988.

- No specific year required, same day each year:	--MMDD
- No specific year required, same month each year:	--MM
- No specific day required:	CCYYMM
- No specific month required:	CCYY

Notes: CCYY = calendar year; MM = month; DD = day.
        In the first two values, the dashes (--) must be included.

#### 2.1.5.1 Seasonal Objects

If it is required to show seasonality of objects, it must be done using the attribute STATUS = 5 (periodic/intermittent). If it is required to encode the start and/or end dates of the season, this must be done using the attributes PERSTA and PEREND.
### 2.1.6 Times

If it is required to show the beginning and end of the active period of tidal objects, it must be encoded using the attributes TIMSTA and TIMEND. When using these attributes, all times must be encoded as Coordinated Universal Time (UTC). The attribute definition for TIMSTA and TIMEND (see Chapter 2 of S-57 Appendix A) states that the mandatory format is CCYYMMDDThhmmss, where T is the separator, and this format must be used.

## 2.2 Data quality description

### 2.2.1 Production information

The producing authority of the ENC must be given in the cell file name and in the “Producing Agency” [AGEN] subfield of the “Data Set Identification” [DSID] field. The use of the meta object M_PROD is prohibited.

### 2.2.2 Up-to-dateness information

Up-to-dateness information must be given in the cell file name extension and in the “Edition Number” [EDTN], “Update Number” [UPDN], “Update Application Date” [UADT] and “Issue Date” [ISDT] subfields of the “Data Set Identification” [DSID] field.

### 2.2.3 Quality, reliability and accuracy of bathymetric data

Information about quality, reliability and accuracy of bathymetric data is given using:
- the meta object M_QUAL for an assessment of the quality of bathymetric data,
- the meta object M_SREL for additional information about the survey,
- the attributes QUASOU, SOUACC and TECSOU on groups of soundings or individual objects,
- the attributes POSACC and QUAPOS on the spatial objects (see clause 2.2.4.1).

For the mariner, M_QUAL provides the most useful information. Therefore, the use of M_QUAL is mandatory for areas containing depth data or bathymetry.

More detailed information about a survey may be given using M_SREL. For example, in incompletely surveyed areas, lines of passage soundings may be indicated as such using a linear M_SREL object. This information is more difficult for the mariner to interpret. Therefore, the use of M_SREL is optional.

For individual objects (wrecks, obstructions etc), or small groups of soundings, QUASOU, SOUACC and TECSOU may be used to provide additional information about quality and accuracy.

#### 2.2.3.1 Quality of bathymetric data

The meta object M_QUAL defines areas within which uniform assessment exists for the quality of bathymetric data, and must be used to provide an assessment of the overall quality of bathymetric data to the mariner. Areas of a cell containing depth data or bathymetry must be covered by one or more M_QUAL, which must not overlap.

Meta object:	Quality of data (M_QUAL)
Attributes:	CATQUA	CATZOC	DRVAL1
DRVAL2 -	the maximum depth to which the quality information applies
POSACC	SOUACC	SURSTA	SUREND	TECSOU	VERDAT
INFORM	NINFOM

Remarks:
- A CATZOC category indicates that the depths encoded within a M_QUAL area meet the minimum criteria described in the CATZOC definition table. A CATZOC category may be further sub-divided by specifying depth and positional accuracy, and sounding technique, using the attributes POSACC, SOUACC and TECSOU, within separate M_QUAL areas.
- DRVAL1 must not be used on a M_QUAL object, unless a swept area occupies the entire M_QUAL area.
- DRVAL2 must not be used on a M_QUAL object, except to specify the maximum depth to which the CATZOC category applies. When DRVAL2 is specified, the CATZOC category applies only to depths equal to or shoaler than DRVAL2. No quality information is provided for depths deeper than DRVAL2.
- POSACC must not be used on a M_QUAL object, except to specify a higher positional accuracy of the depths than the CATZOC category indicates. When DRVAL1 is specified, POSACC must not be used - there is no positional accuracy information provided for any underlying depths in this circumstance.
- SOUACC must not be used on a M_QUAL object, except to specify a higher accuracy of the depths than the CATZOC category indicates. When DRVAL1 is specified, SOUACC refers only to the accuracy of the swept depth defined by DRVAL1 - there is no depth accuracy information provided for any underlying depths in this circumstance.
- When the M_QUAL area contains soundings of two or more different techniques, the attribute TECSOU must not be used.
- When the M_QUAL area contains data from only one survey, the date of survey, if required, must be specified using the attribute SUREND. When the M_QUAL area contains data from two or more surveys, the date of the oldest survey, if required, must be specified using the attribute SURSTA, and the date of the most recent survey, if required, must be specified using SUREND.
- Additional quality information may be given using the meta object M_SREL.
- Where M_QUAL areas are encoded over land, CATZOC should be set to 6 (unassessed).
- M_QUAL may either be encoded over wet areas only, or alternatively a single M_QUAL object may be created for the whole cell over wet and dry areas.
- When M_QUAL and the meta object M_ACCY are encoded in a cell, they should not overlap.
- When both M_QUAL and M_ACCY objects are used in a cell, the area covered by these objects should equal the area of data coverage for the cell.
- POSACC on the M_QUAL applies to bathymetric data situated within the area, while QUAPOS or POSACC on the associated spatial objects, qualifies the location of the M_QUAL object itself.

#### 2.2.3.2 Survey reliability

The survey reliability may be encoded using the meta object M_SREL.

Meta object:	Survey reliability (M_SREL)
Attributes:	QUAPOS	QUASOU	SCVAL1	SCVAL2	SDISMN	SDISMX	SURATH	SUREND	SURSTA	SURTYP	TECSOU	INFORM	NINFOM

Remarks:
- If the attributes SOUACC and TECSOU are required, they must be encoded on either the meta object M_QUAL or on individual geo objects (e.g. SOUNDG).
- If it is required to encode information to indicate the source of a survey, it must be done using the attribute SURATH on M_SREL (see clause 2.2.5.1).
- QUAPOS on the M_SREL applies to bathymetric data situated within the area, while QUAPOS or POSACC on the associated spatial objects, qualifies the location of the M_SREL object itself.

#### Quality of sounding

If it is required to encode the quality of sounding, it must be done using the attribute QUASOU on either the meta object M_SREL or on individual geo objects (e.g. SOUNDG).

The quality of sounding must not be encoded using QUASOU on the depth geo object, unless it is different to the value of QUASOU encoded on M_SREL (see tables 5.1 and 6.4).

#### Sounding accuracy

Sounding accuracy is encoded using the attribute CATZOC on the meta object M_QUAL. If it is required to encode additional sounding accuracy information (see clauses 2.2.3.1 and 5.6), it must be done using the attribute SOUACC on either the meta object M_QUAL or on individual geo objects (e.g. SOUNDG).

The accuracy of sounding must not be encoded using SOUACC on the depth geo object, unless it is different to the value of SOUACC encoded on M_QUAL.

#### Technique of sounding measurement

If it is required to encode the technique of sounding measurement, it must be done using the attribute TECSOU on either the meta object M_QUAL or on individual geo objects (e.g. SOUNDG).

The technique of sounding measurement must not be encoded using TECSOU on the depth geo object, unless it is different to the value of TECSOU encoded on M_QUAL.

### 2.2.4 Accuracy of non-bathymetric data

#### 2.2.4.1 Quality of positions

The meta object M_ACCY may be used to provide an overall accuracy of position for all non-bathymetric features. It must not be used to provide the accuracy of bathymetric information.

Meta object:	Accuracy of data (M_ACCY)
Attributes:	HORACC	POSACC	SOUACC	VERACC	INFORM	NINFOM

The attributes QUAPOS and POSACC may be applied to any spatial object, in order to qualify the location of an object.

QUAPOS and POSACC must not be applied to the spatial object of any geo object if they are identical to the QUAPOS and POSACC values of the underlying meta object.

QUAPOS gives qualitative information, whereas POSACC gives quantitative information.

POSACC on the M_ACCY applies to non bathymetric data situated within the area, while QUAPOS or POSACC on the associated spatial objects, qualifies the location of the M_ACCY object itself.

Meta objects M_ACCY and M_QUAL should not overlap.

#### 2.2.4.2 Horizontal accuracy

If it is required to encode the accuracy of a horizontal clearance (attribute HORCLR), it must be done using the attribute HORACC.

HORACC applies only to HORCLR. There is no attribute to express the accuracy of the attributes HORLEN and HORWID.

#### 2.2.4.3 Vertical accuracy

If it is required to encode the accuracy of a vertical clearance (attributes VERCLR, VERCOP, VERCSA, VERCCL), it must be done using the attribute VERACC.

If several vertical clearances are given for one object, the accuracy given must be that of the least accurate.

### 2.2.5 Source of data

#### 2.2.5.1 Source of bathymetric data

Details of the source surveys used in compilation may be encoded using the meta object M_SREL, as described in clause 2.2.3.2.

Remarks:
- If it is required to encode details of the survey authority, it must be done using the attribute SURATH, and must not be encoded using the attribute SORIND.
- If an object has a source different to that given by the underlying M_SREL, this other source should be encoded using both the attributes SORIND and SORDAT on the object, but only if this information is considered to be useful to the mariner.

#### 2.2.5.2 Source of other data

The source of non-bathymetric information should be encoded using both the attributes SORIND and SORDAT on the individual objects, but only if this information is considered to be useful to the mariner.

### 2.2.6 Compilation scale

The default value for the entire data set must be given in the “Compilation Scale of Data” [CSCL] subfield of the “Data Set Parameter” [DSPM] field. The default value should be the compilation scale appropriate to the greater part of the data in the cell.

If the compilation scale for an area is different to the value given in the CSCL subfield for the data set, it must be encoded using the meta object M_CSCL. The areas covered by these meta objects must not overlap.

Meta object:	Compilation scale of data (M_CSCL)
Attributes:	CSCALE	INFORM	NINFOM

Remarks:
The compilation scale provides the reference value for the overscale indication on an ECDIS.

### 2.2.7 Use of the attribute SCAMIN

The SCAMIN value of an object determines the display scale below which the object is no longer displayed. Its purpose is to reduce clutter, to prioritise the display of objects and to improve display speed. In encoding its value, the producing authority should consider these factors, as well as the scale at which the object is no longer likely to be required for navigation.

In order to optimise the performance and clarity of the ENC, it is strongly recommended that SCAMIN is used.

Remarks:
- SCAMIN only affects the display of an object on an ECDIS, not its presence in the SENC.
- If SCAMIN is not encoded, the object is displayed at all scales.
- Where SCAMIN is used, it must always be set to a scale less (i.e. to a smaller scale) than or equal to the compilation scale of the data as described in clause 2.2.6 above. Failure to follow this rule will mean that objects will not be displayed on screen until the overscale warning is activated.
- Group 1 and Meta objects must always be displayed. Therefore, SCAMIN must not be encoded on Group 1 and Meta objects.
- If the same object exists in cells of different navigational purposes, the same SCAMIN value should be assigned to each occurrence of the object.

## 2.3 Textual information

The attributes INFORM, NINFOM, TXTDSC and NTXTDS should not be used when it is possible to encode the information by means of any other attribute. However, for reasons of backward compatibility with the S-57 Object Catalogue Edition 3.0, attribute values which appear for the first time in the S-57 Object Catalogue Edition 3.1, must have their meaning described in INFORM (e.g. wellhead mark).

INFORM and NINFOM contain information as text, whereas TXTDSC and NTXTDS encode the name of an external file.

The text contained in INFORM and NINFOM is ASCII text. Formatting characters (C0 as defined in S-57 Part 3, Annex B) are prohibited. INFORM and NINFOM should generally be used for short notes (e.g. caution notes from paper charts), or to transfer information which cannot be encoded by other attributes, or to give more detailed information about an object.

The text files referenced by TXTDSC and NTXTDS must be ASCII files, and may contain formatted text. These files should generally be used for longer texts (e.g. longer chart notes, tables or paragraphs from sailing directions). It is up to the producing authority to determine the most suitable means of encoding a particular piece of text.

## 2.4 Colours and colour patterns

If it is required to encode multiple colours on an object, they must be interpreted and encoded using the attributes COLPAT and COLOUR as follows:

- For horizontal stripes (COLPAT = 1), the first colour in the list must be the top-most, and subsequent colours follow sequentially from top to bottom. For example, COLOUR = 3,1 to encode a red stripe above a white stripe.
- For vertical stripes (COLPAT = 2), the first colour in the list must be the left-most, and subsequent colours follow sequentially from left to right. For example, COLOUR = 3,1,3 to encode red, white, red vertical stripes.
- For diagonal stripes (COLPAT = 3), the first colour in the list must be the top-left-most and subsequent colours follow sequentially from top left to bottom right. For example, COLOUR = 1,3,1,3,1 to encode white, red, white, red, white diagonal stripes.
- For squares (COLPAT = 4), the first colour in the list must be the top-left-most square. Subsequent colours follow sequentially from left to right along the top row then repeated for subsequent rows until the bottom right-most square is reached. For example, COLOUR = 1,3,3,1 to encode white, red squares on the top row, and red, white squares on the bottom row.
- For border stripes (COLPAT = 6), the first colour in the list must be the border stripe, the second colour must be that of the background. For example, COLOUR = 3,1 to encode a red border stripe on a white background. Where a border stripe is combined with other patterns, the border stripe must be the first colour in the list, and subsequent colours must be interpreted in accordance with the rules defined for the additional patterns. Therefore, if a pattern contains a border stripe as well as other patterns, the border stripe must be the first value in the list of COLPAT.

## 2.5 Reference to other publications

If it is required to encode a reference to other nautical information or publications, it must be done using the meta object M_NPUB.

Meta object:	Nautical publication information (M_NPUB)
Attributes:	INFORM	NINFOM

Remarks:
References to nautical publications in M_NPUB, must be encoded using the attribute PUBREF, and references to external picture files must be encoded using the attribute PICREP.

## 2.6 Updating

### 2.6.1 Issuing updates in advance

Under certain conditions, it may be necessary for a data producer to issue update information in advance. For example, a change in a traffic routeing system must be made public before the new situation is implemented. Within an ER data set there is no means of indicating the date at which an update must be applied. Therefore, when an ER data set is received by an end user, it must be applied immediately. To avoid situations where update information would cause target data to reflect a situation that does not yet exist, the following coding rules must be followed:

a)	If the advance update information contained in the update message involves the addition of objects to the existing data (e.g. a new lighthouse), the attribute DATSTA on the new objects must contain the date at which the update becomes active.

b) If the advance update information contained in the update message involves the modification of existing objects (e.g. a change in a traffic routeing system), it must be treated as a deletion of the existing objects and replacement with new objects. See a) above and c) below.

c) If the advance update information contained in the update message involves the deletion of existing objects (e.g. the removal of a buoy), the update message must set the DATEND attribute of all objects to be deleted to the date at which the update becomes active. NB. This update message does not actually delete the objects from the data set, it simply indicates that on the date held in DATEND they become obsolete. A further update to actually delete the obsolete objects from the data set should be sent at the time that the change in the real world occurs.

d) To highlight to the mariner that the advance update information contained in an update message will take place in the future, it is recommended that a caution area object (CTNARE) be created covering the location at which the future changes will take place. A warning note specifying, in plain language, the nature of the future change should be encoded, either in the attribute INFORM or in a file referenced by the TXTDSC attribute of the CTNARE. The attribute DATEND on the CTNARE must be set to the date at which the change described in the update becomes active.

Changes to DATSTA and DATEND cannot be applied to spatial objects. Therefore, a change to the geometry of a real world object (e.g. the relocation of a buoy) to be applied in the future can only be achieved by updating all of the feature and spatial objects involved.

As a consequence of issuing advance information updates, more than one instance of a particular real world object could exist in the data set.

## 2.7 Multiple objects

On some sources, multiple objects in close proximity are generalised to a single object with a text string indicating the presence of the other objects. In such cases, one object of the appropriate class should be encoded and the true number of objects should be encoded using the attribute INFORM (e.g. 3 chimneys). If the true number of objects is not known, the text ”more than one” should be encoded using INFORM.

For the encoding of multiple, identical lights using the attribute MLTYLT, see table 12.3 in clause 12.8.7.

For the encoding of leading lights that are merged on the source document, see clause 12.8.6.4.

  1. Minimal depiction areas (see M4 - §404)

Where minimal depiction areas exist within a specified ENC navigational purpose, they should be encoded using one of the following options:

2.8.1	Wide blank areas

Areas of a data set which contain no data must be covered using the meta object M_COVR, with attribute CATCOV = 2 (no coverage available).

    1. Simplified or minimal depiction areas

- Bathymetry in such areas should be encoded as described in clause 5.8.3.
- Information that does not relate to bathymetry but is relevant to Group 1 objects (islands, shoreline constructions, floating docks, hulks etc) may be encoded.
One CTNARE object covering the whole area should be created. The attributes INFORM or TXTDSC should be encoded using one of the following options (the textual content of the attributes is within quotation marks and italicised):

Where larger scale coverage is available:

“Most features, including bathymetry, are omitted in this area. The minimal depiction of detail in this area does not support safe navigation, mariners should use a more appropriate navigational purpose.”
Any other information contained in chart notes pertaining to the area should be incorporated within, or replace completely, the above statement.

Where no larger scale coverage is available:

“Most features, including bathymetry, are omitted in this area. The minimal depiction of detail in this area does not support safe navigation.”
This statement should be supplemented by additional cautionary information from chart notes relating to any authority to be consulted before navigating in the area.

# 3. Time Varying Objects

## 3.1 Magnetic data (see M4 - §270)

### 3.1.1 Magnetic variation

Until a world magnetic model is universally available for inclusion in ECDIS, if it is required to encode magnetic variation, it must be done using the object class MAGVAR. As a minimum, updates should be supplied to coincide with changes of epoch (i.e. every five years).

Geo object:	Magnetic variation (MAGVAR)
Attributes:	DATEND	DATSTA	RYRMGV	VALACM	VALMAG	INFORM	NINFOM

### 3.1.2 Abnormal magnetic variation (see M4 - §274)

If it is required to encode an abnormal magnetic variation in a localised area, it must be done using the object class LOCMAG.

Geo object:	Local magnetic anomaly (LOCMAG)
Attributes:	NOBJNM	OBJNAM	VALLMA	INFORM	NINFOM

If the area cannot be defined, the feature should be represented as a point object.

When the deviation for an area makes reference to a range rather than a specific value, the range of values should be indicated using the attribute INFORM (e.g. From -27 degrees to 3 degrees)

## 3.2 Tidal data (see M4 - §406)

The inclusion of tidal information in ENC data sets is optional.

For Standard Ports the appropriate national HO or an organisation authorised by it should provide the predictions.

For Secondary Ports, the appropriate HO or an organisation authorised by it should, where possible, provide the predictions. Should such predictions not be available, the ECDIS manufacturer should approach the appropriate national HO for advice regarding the best methods of prediction for the Secondary Ports in its area of responsibility.

It is recommended that each appropriate HO, or an organisation authorised by it, should determine the spatial limits for applying tidal information where applicable, and the number of tidal stations to be used in modelling. The HOs should be responsible for determining the best methodologies to be used in their areas of responsibility.

Where tidal information is encoded, it must be assessed to a minimum confidence level of 95%, irrespective of the method of application or its source.

### 3.2.1 Time series data

If it is required to encode times and heights of high and low waters, it must be done using the object class T_TIMS. In addition, where the data is available, a regular time series of tidal heights should also be encoded using this object class.

Geo object:	Tide-time series (T_TIMS)
Attributes:	NOBJNM	OBJNAM
TIMEND	TIMSTA -	specify the period for which the time series is valid
T_ACWL	T_TSVL	T_TINT	T_HWLW	STATUS	INFORM	NINFOM

### 3.2.2 Prediction by harmonic methods

If it is required to encode the parameters for the prediction of tidal heights using harmonic methods, it must be done using the object-class T_HMON. The supplier of parameters should be consulted on how to use this data, and which calculation algorithms to use with the data.

Geo object:	Tide-harmonic prediction (T_HMON)
Attributes:	NOBJNM	OBJNAM	T_ACWL
T_MTOD -	1 - simplified harmonic method of tidal prediction
2 - full harmonic method of tidal prediction
T_VAHC	STATUS	INFORM	NINFOM

### 3.2.3 Prediction by non-harmonic methods

If it is required to encode the parameters for the prediction of tidal heights using time and height differences, it must be done using the object class T_NHMN.

The reference port to be used for these predictions must be identified using a collection object (C_ASSO) between the tidal parameter object T_TIMS or T_HMON of the reference port, and the tidal parameter object T_NHMN of the secondary port. If the reference port is not located within the data set or exchange set, then its tidal parameters should be supplied as a geo object with no geometry.

Other non-harmonic methods for predicting tidal heights are not currently supported.

Geo object:	Tide-non-harmonic prediction (T_NHMN)
Attributes:	NOBJNM	OBJNAM	T_ACWL
T_MTOD -	3 – time and height differences non-harmonic method
T_THDF	STATUS	INFORM	NINFOM

3.3	Tidal stream data (see M4 - §407)

### 3.3.1 Tidal stream (flood/ebb)

If it is required to encode tidal stream information that is limited to flood and ebb directions and/or values, it must be done using the object class TS_FEB.

Geo object:	Tidal stream-flood/ebb (TS_FEB)
Attributes:	CAT_TS
CURVEL -	maximum rate (during springs)
DATEND	DATSTA	NOBJNM	OBJNAM	ORIENT	PEREND	PERSTA
INFORM	NINFOM

### 3.3.2 Tidal stream time series

If it is required to encode time series data for tidal streams, it must be done using the object class TS_TIS.

Geo object:	Tidal stream - time series (TS_TIS)
Attributes:	NOBJNM	OBJNAM
TIMEND	TIMSTA -	specify the period for which the time series is valid
TS_TSV	T_TINT	STATUS	INFORM	NINFOM

### 3.3.3 Prediction by harmonic methods

If it is required to encode parameters for the prediction of tidal streams using harmonic methods, it must be done using the object class TS_PRH. The supplier of parameters should be consulted on how to use this data, and which calculation algorithms to use with the data.

Geo object:	Tidal steam - harmonic prediction (TS_PRH)
Attributes:	NOBJNM	OBJNAM
T_MTOD -	1 - simplified harmonic method of tidal prediction
2 - full harmonic method of tidal prediction
T_VAHC	STATUS	INFORM	NINFOM

### 3.3.4 Prediction by non-harmonic methods

If it is required to encode parameters for the prediction of tidal streams using time and rate, it must be done using the object class TS_PNH.

The reference station to be used for these predictions must be identified using a collection object (C_ASSO) between the stream parameter object TS_TIS or TS_PRH of the reference station, and the stream parameter object TS_PNH of the secondary station. If the reference station is not located within the data set or exchange set, then its tidal stream parameters should be supplied as a geo object with no geometry.

Other non-harmonic methods for predicting tidal stream are not currently supported.

Geo object:	Tidal steam - non-harmonic prediction (TS_PNH)
Attributes:	NOBJNM	OBJNAM	T_THDF
T_MTOD	-	3 – time and height differences non-harmonic method
STATUS	INFORM	NINFOM

### 3.3.5 Tidal stream panels

If it is required to encode the information generally shown on paper charts as a tidal stream panel and stations, it must be done using the object class TS_PAD.

Tidal stream values encoded in this way should be mean spring rates, i.e. the tidal stream rates associated with a tidal range which is defined as the difference in height between MHWS and MLWS.

Geo object:	Tidal steam panel data (TS_PAD)
Attributes:	NOBJNM	OBJNAM	TS_TSP	INFORM	NINFOM

## 3.4 Current data

If it is required to encode a non-gravitational current, it must be done using the object class CURENT.

Geo object:	Current (CURENT)
Attributes:	CURVEL	DATEND	DATSTA	NOBJNM	OBJNAM	ORIENT	PEREND
PERSTA	INFORM	NINFOM

# 4. Topography

## 4.1 Land area

Mangrove areas or land areas that are never covered by the sea must be encoded using the object class LNDARE.

Rivers, canals, lakes, basins and docks, which are not navigable at compilation scale, must be encoded on top of LNDARE or UNSARE objects (see clause 5.4.8) .

LNDARE objects of type area are part of Group 1.

Geo object:	Land area (LNDARE)
Attributes:	CONDTN	OBJNAM	NOBJNM	INFORM	NINFOM	STATUS

Remarks:
- If it is required to describe the natural scenery of the land, it must be done using the object class LNDRGN (see clause 4.7.1).
- LNDARE is usually of type area; it may, however, be of type point (e.g. islet, rock that does not cover), or of type line (e.g. islet, offshore bar, isthmus).

## 4.2 Vertical measurements (see M4 - §302 and §303)

### 4.2.1 Vertical datum

See clause 2.1.2.

### 4.2.2 Heights and elevations

If it is required to encode the altitude of natural features (e.g. hills, coastlines, slopes), with the exception of trees, it must be done using the attribute ELEVAT (figure 1 - a).

For artificial features (e.g. landmarks, buildings) or trees:
- If it is required to encode the altitude of the ground level at the base of the object, it must be done using ELEVAT (figure 1 - b).
- If it is required to encode the altitude of the highest point of the object, it must be done using the attribute HEIGHT (figure 1 - c).
- If it is required to encode the height of the object above ground level, it must be done using the attribute VERLEN (figure 1 - d).

Figure 1 – Heights and elevations

## 4.3 Control points (see M4 - §304 to §306)

If it is required to encode a control point, it must be done using the object class CTRPNT.

Geo object:	Control point (CTRPNT)
Attributes:	CATCTR	DATEND	DATSTA	ELEVAT	NOBJNM	OBJNAM	VERACC
VERDAT	INFORM	NINFOM

## 4.4 Distance marks (see M4 - §307)

If it is required to encode a distance mark, it must be done using the object class DISMAR.

Geo object:	Distance mark (DISMAR)
Attributes:	CATDIS	DATEND	DATSTA	NOBJNM	OBJNAM
INFORM -	the value of distance with its unit of measurement
NINFOM

## 4.5 Coastline

In all cases the coastline must be encoded using either COALNE or SLCONS (line or area) objects. These features form the border of the land area (LNDARE) object.

Natural sections of coastlines, lakeshores and river banks should be encoded as COALNE, whereas artificial sections of coastlines, lake shores, river banks, canal banks and basin borders should be encoded as SLCONS. The exception to this general rule is when a lake, river, canal, or basin is not navigable at the compilation scale, in which case the boundaries must not be encoded as COALNE or SLCONS (see clauses 4.6.6.3, 4.6.6.5, 4.7.6, 4.7.8, 4.8.1).

### 4.5.1 Natural coastline (see M4 - §312)

Geo object:	Coastline (COALNE)
Attributes:	CATCOA	COLOUR	CONRAD	CONVIS	ELEVAT	NOBJNM	OBJNAM	VERACC	VERDAT	INFORM	NINFOM

Spatial objects associated with unsurveyed coastlines (see M4 - §311) should be encoded using spatial attribute QUAPOS = 2 (unsurveyed).

If it is required to encode a description of the nature of the coastline, it must be done using the attribute CATCOA. Other area objects may be used to describe the land region adjacent to the coastline (see clause 4.7).

### 4.5.2 Artificial coastline (see M4 - §313 and §320)

Geo object:	Shoreline construction (SLCONS)
Attributes:	CATSLC	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA	HEIGHT
HORACC -	applies to HORCLR
HORCLR	HORLEN	HORWID	NATCON	NOBJNM	OBJNAM	STATUS
VERACC	VERDAT	VERLEN	WATLEV	INFORM	NINFOM
Figure 2 represents a shoreline construction such as a mole, including a berthing facility (INT1 - IF12), with a relatively flat top (abcdlmna), and sloping sides partly above high water (nmldefgn) and partly intertidal (dopqrhgfed).

Figure 2 – Shoreline constructions
Remarks:
Each of the three parts of the shoreline construction may be encoded as separate SLCONS objects of type area, and the masked line (an) is optional. Alternatively, the boundaries of the shoreline construction may be encoded as SLCONS objects of type line, and, if part of the SLCONS boundary has a different characteristic (e.g. (bc) attribute CATSLC = 6 or 15), it should be encoded as a separate SLCONS object of type line.
- In this example, the shoreline construction area above the high water line must also be covered by a LNDARE object of type area, and the intertidal shoreline construction area must also be covered by a DEPARE object of type area.
- SLCONS objects should be broken into their constituent parts, and categorised using attributes such as CATSLC and WATLEV as indicated on the source.
- If the presence of an object is only indicated on the source by a textual reference, without a clear symbol (e.g. ‘pier’, ‘groyne’, ‘post’), it should be encoded using a CTNARE object with the textual reference encoded using the attribute INFORM.
- Intertidal or submerged artificial rock walls, such as training walls that are not attached to the shoreline, should be encoded using the appropriate value for CATSLC, and WATLEV = 3 (always under water/submerged) or WATLEV = 4 (covers and uncovers).

## 4.6 Harbour installations

### Harbour facilities

If it is required to encode a harbour facility, it must be done using the object class HRBFAC.

Geo object:	Harbour facility (HRBFAC)
Attributes:	CATHAF	CONDTN	DATEND	DATSTA	NATCON	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM	NINFOM

Remarks:
Depending on the navigational purpose, harbour facilities are defined by: an area including docks, basins, and dockside equipment, or a point.

### Berths (see M4 - §323)

If it is required to encode a berth, it must be done using the object class BERTHS.

Geo object:	Berth (BERTHS)
Attributes:	DATEND	DATSTA
DRVAL1 -	minimum depth at the berth
NOBJNM	OBJNAM -	name or number of the berth
PEREND	PERSTA	QUASOU	SOUACC	STATUS	VERDAT
INFORM -	maximum draft permitted at the berth (e.g. Maximum draft permitted = 14 metres)
NINFOM

Remarks:
- The berth encodes the named place where a vessel can be moored adjacent to a shoreline construction. The shoreline construction itself should be encoded using the object class SLCONS (see clause 4.5.2).
- Landing places for boats should be encoded as small craft facilities (see clause 4.6.5).

### 4.6.3 Harbour offices (see M4 - §325)

If it is required to encode a harbour office, it must be done using the object class BUISGL (see clause 4.8.15), with the attribute FUNCTN taking at least one of the values:

2	- harbour-master’s office
3	- custom office
4	- health office
11	- pilot office

### 4.6.4 Checkpoints

If it is required to encode a checkpoint, it must be done using the object class CHKPNT.

Geo object:	Checkpoint (CHKPNT)
Attributes:	CATCHP	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM
Remarks:
The CHKPNT must only be used to encode the function. In addition, if it is required to encode a physical object (e.g. building), it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).

### Small craft facilities

If it is required to encode a small craft facility, it must be done using the object class SMCFAC.

Geo object:	Small craft facility (SMCFAC)
Attributes:	CATSCF	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM
NINFOM

Remarks:
The SMCFAC must only be used to encode the function. In addition, if it is required to encode a physical object (e.g. building, mooring buoy), it must be done using an appropriate object class (e.g. BUISGL, MORFAC).

### 4.6.6 Docks
#### Dry docks (see M4 - §326.1)

If it is required to encode a dry dock, it must be done using the object class DRYDOC.

Geo object:	Dry dock (DRYDOC)
Attributes:	CONDTN
DRVAL1 -	minimum depth in the dock when the gate is open.
HORACC -	applies to HORCLR
HORCLR	HORLEN	HORWID	NOBJNM	OBJNAM	QUASOU	SOUACC
STATUS	VERDAT
INFORM -	maximum draft permitted in the dock (e.g. Maximum draft permitted = 6 metres)
NINFOM

Remarks:
A dry dock must also be covered by a LNDARE object. The boundary of a dry dock must not be encoded as a separate object (COALNE or SLCONS), except for the gate object (GATCON), which may be encoded.

#### 4.6.6.2 Floating docks (see M4 - §326.2)

If it is required to encode a floating dock, it must be done using the object class FLODOC.

Geo object:	Floating dock (FLODOC)
Attributes:	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA
DRVAL1
HORACC -	applies only to HORCLR
HORCLR	HORLEN	HORWID	LIFCAP	NOBJNM	OBJNAM	STATUS
VERACC	VERDAT	VERLEN
INFORM -	maximum draft permitted in the dock (e.g. Maximum draft permitted = 6 metres)
NINFOM

Remarks:
FLODOC of type area are part of Group 1.

#### 4.6.6.3 Tidal and non-tidal basins (see M4 - §326.3 and §326.4)

Geo object:	Dock area (DOCARE)
Attributes:	CATDOC	CONDTN	DATEND	DATSTA
HORACC -	applies only to HORCLR
HORCLR -	size of the entrance
NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

Remarks:
- If the dock is navigable at compilation scale, it must be encoded using the object classes DEPARE or DRGARE (see clause 5.4.8), and the geo objects making up the dock limits must be encoded using appropriate object classes such as COALNE, SLCONS or GATCON. The dock must not be encoded as DOCARE. If it is required to encode the name of the dock, it must be done using the object class SEAARE.
- If it is required to encode a dock which is not navigable at compilation scale, it must be done using the object class DOCARE, covered by a LNDARE or UNSARE object. The name of the dock should be encoded using the attribute OBJNAM on the DOCARE. The boundary of a dock must not be encoded as a separate object (e.g. COALNE, SLCONS), except for the gate object (GATCON), which may be encoded.
- In a non-tidal basin, depths may refer to a sounding datum different to that in open waters. If this area is navigable at the compilation scale, the value of this datum must be encoded using the meta object M_SDAT, with attribute VERDAT = 24 (local datum).
- In reality, smaller dock areas may be included in major dock areas, with different names or characteristics. To encode this fact, dock areas (DOCARE) and/or sea areas (SEAARE) may overlap.

4.6.6.4	Gates (see M4 - §326.5 to §326.7)

If it is required to encode a gate that controls the flow of water, it must be done using the object class GATCON.

Geo object:	Gate (GATCON)
Attributes:	CATGAT	CONDTN
DRVAL1 -	minimum depth over the sill
HORACC -	applies only to HORCLR
HORCLR	NATCON	NOBJNM	OBJNAM	QUASOU	SOUACC	STATUS
VERACC -	applies only to VERCLR
VERCLR
VERDAT -	applies only to VERCLR (not DRVAL1)
INFORM	NINFOM

GATCON of type area must also be covered by a DEPARE or LNDARE object.

4.6.6.5	Locks

If it is required to encode a lock basin, it must be done using the object class LOKBSN.

Geo object:	Lock basin (LOKBSN)
Attributes:	DATEND	DATSTA
HORACC -	applies only to HORCLR
HORCLR	HORLEN	HORWID	NOBJNM	OBJNAM	STATUS	INFORM
NINFOM

Remarks:
- If the lock is navigable at compilation scale, it must be encoded using the object classes DEPARE or DRGARE (see clause 5.4.8), and the geo objects making up the limits of the lock must be encoded using appropriate object classes such as COALNE, SLCONS or GATCON. The lock must not be encoded as LOKBSN. If it is required to encode the name of the lock, it must be done using the object class SEAARE.
- If it is required to encode a lock that is not navigable at compilation scale, it must be done using LOKBSN covered by a LNDARE or UNSARE object. The name of the lock should be encoded using the attribute OBJNAM on the LOKBSN object.
- The gates should be encoded as a GATCON object with attribute CATGAT = 4 (lock gate) or 3 (caisson). At small scale, a lock may be encoded using GATCON only, without using LOKBSN.

#### 4.6.6.6 Gridirons (see M4 - §326.8)

If it is required to encode a gridiron, it must be done using the object class GRIDRN.

Geo object:	Gridiron (GRIDRN)
Attributes:	HORACC	HORLEN	HORWID	NATCON	NOBJNM	OBJNAM	STATUS	VERACC	VERLEN	WATLEV	INFORM	NINFOM

### 4.6.7 Mooring / warping facilities and pontoons
#### 4.6.7.1 Mooring / warping facilities (see M4 - §327)

If it is required to encode a mooring/warping facility, it must be done using the object class MORFAC.

Geo object:	Mooring / warping facility (MORFAC)
Attributes:	BOYSHP -	used only if CATMOR = 7
CATMOR	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS
DATEND	DATSTA	HEIGHT	NATCON	NOBJNM	OBJNAM
PEREND	PERSTA	STATUS	VERACC	VERDAT	VERLEN
WATLEV	INFORM	NINFOM

Remarks:
If it is required to encode a pile or post that is used as a mooring post, it must be done using MORFAC, with attribute CATMOR = 5 (pile or post). If the pile or post is not used as a mooring post, see clause 4.6.7.2.
·	Stumps of mooring posts dangerous to navigation must be encoded using the object class OBSTRN, with attribute CATOBS = 1 (snag/stump). If such stumps are not dangerous to navigation, they must be encoded using MORFAC, with attributes CATMOR = 5 (pile or post) and CONDTN = 2 (ruined).
A MORFAC object of type area, with attribute WATLEV = 1, 2 or 6 must also be covered by a LNDARE object.

#### 4.6.7.2 Piles

If it is required to encode a pile or post that is not used as a mooring/warping facility, it must be done using the object class PILPNT.

Geo object:	Pile (PILPNT)
Attributes:	CATPLE	COLOUR	COLPAT	CONDTN	CONVIS	DATEND	DATSTA
HEIGHT	NOBJNM	OBJNAM	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
- Stumps of piles or posts that are dangerous to navigation must be encoded using OBSTRN objects, with attribute CATOBS = 1 (snag/stump), and must not be encoded using PILPNT.
- See clause 4.6.7.1 for details of how to encode a pile or post that is used as a mooring/warping facility.

#### 4.6.7.3 Pontoons (see M4 - §326.9)

If it is required to encode a pontoon, it must be done using the object class PONTON.

Geo object:	Pontoon (PONTON)
Attributes:	CONDTN	CONRAD	CONVIS	DATEND	DATSTA	NATCON
NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	VERACC
VERLEN	INFORM	NINFOM

Remarks:
PONTON objects of type area are part of Group 1.
### 4.6.8 Hulks

If it is required to encode a hulk, it must be done using the object class HULKES.

Geo object:	Hulk (HULKES)
Attributes:	CATHLK	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS
HORACC	HORLEN	HORWID	NOBJNM	OBJNAM	VERACC
VERLEN	INFORM	NINFOM

Remarks:
HULKES objects of type area are part of Group 1.

### 4.6.9 Dockside buildings and structures
#### 4.6.9.1 Transit sheds and warehouses (see M4 - §328.1)

If it is required to encode a transit shed or warehouse, it must be done using a BUISGL object (see clause 4.8.15), with attributes FUNCTN = 15 (transit shed/warehouse), and if it is required, OBJNAM = name or number of the shed.

#### 4.6.9.2 Timber yards (see M4 - §328.2)

If it is required to encode a timber yard, it must be done using a PRDARE object (see clause 4.8.13), with attribute CATPRA = 6 (timber yard).

#### 4.6.9.3 Cranes (see M4 - §328.3)

If it is required to encode a crane, it must be done using the object class CRANES.

Geo object:	Crane (CRANES)
Attributes:	CATCRN	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	HEIGHT
LIFCAP	NOBJNM	OBJNAM
ORIENT -	angular distance from true north to the axis of the crane’s jib (generally perpendicular to the wharf)
RADIUS	STATUS
VERACC -	applies only to VERCLR (not HEIGHT)
VERCLR
VERDAT -	applies only to VERCLR (not HEIGHT)
VERLEN	INFORM	NINFOM

Remarks:
The position of a sheerleg or a travelling crane is defined as its resting position. If it is required to encode the track, it must be done using the object class RAILWY (see clause 4.8.2).

### 4.6.10 Works in progress and projected (see M4 - §329)

Features that are under construction or projected should be encoded in the same way as existing features (e.g. using LNDARE, SLCONS, DRYDOC, PIPSOL objects), with the attributes:

CONDTN -	1 - under construction
3 - under reclamation
5 - planned construction
SORDAT -	year or date of the information

The coastline existing before the beginning of the works should remain encoded as a COALNE or SLCONS object until the completion of the works.

## 4.7 Natural features (see M4 - §350)

### 4.7.1 Natural sceneries

If it is required to describe the natural scenery of the land, or to give the geographic name of an area on land, it should be encoded using the object class LNDRGN.

Geo object:	Land region (LNDRGN)
Attributes:	CATLND	NATQUA	NATSUR	NOBJNM	OBJNAM	WATLEV	INFORM
NINFOM

Remarks:
- This object class has a use similar to that of the object class SEAARE (see clause 8), but for the land.
- A LNDRGN area should be bounded, if possible, by existing lines used by other objects (e.g. COALNE). If necessary, however, this area may be bounded by other lines created to close the area, or to describe a new area.
- For capes, points, peninsulas and other types of LNDRGN where there is no specific value for the attribute CATLND, the generic term "Cape", "Point", "Peninsula", etc may be included on the attributes OBJNAM and NOBJNM.
- LNDRGN objects of type area may overlap.
- A LNDRGN object of type area must be covered by objects from Group 1 (LNDARE, DEPARE, UNSARE etc).

### 4.7.2 Height contours, spot heights (see M4 - §351)

If it is required to encode a height contour or spot height, it must be done using the object class LNDELV.

Geo object:	Land elevation (LNDELV)
Attributes:	CONVIS	ELEVAT	NOBJNM	OBJNAM	VERACC	VERDAT	INFORM	NINFOM

Height contours are associated with line spatial objects, whereas spot heights are associated with point spatial objects.

Spatial objects associated with approximate contours or spot heights should be encoded using the attribute QUAPOS = 4 (approximate).

### 4.7.3 Marsh (see M4 - §312.2)

If it is required to encode a marshy area behind the coastline, it must be done using a LNDRGN object, with attribute CATLND = 2 (marsh).

If the seaward edge of a marsh area is coincident with the coastline, the coastline should be encoded as a COALNE object, with attribute CATCOA = 8 (marshy shore), and the coastline’s spatial object should have the attribute QUAPOS = 4 (approximate) for the visible coastline.

### 4.7.4 Dunes, sand hills (see M4 - §312.3)

If it is required to encode a dune or sand hill, it must be done using the object class SLOGRD.

Geo object:	Sloping ground (SLOGRD)
Attributes:	CATSLO -	3 - dune
4 - hill
COLOUR	CONRAD	CONVIS	NATCON	NATQUA	NATSUR
NOBJNM	OBJNAM	INFORM	NINFOM

If these features are positioned along the coastline, a COALNE object must also be created.

If it is required to encode the height of one of these features, a LNDELV object must also be created.

### 4.7.5 Cliffs (see M4 - §312.1)

If it is required to encode a cliff, it must be done using a SLOGRD object (see clause 4.7.4), with attribute CATSLO = 6 (cliff) and / or using the object class SLOTOP.

Geo object:	Slope topline (SLOTOP)
Attributes:	CATSLO -	6 - cliff
COLOUR	CONRAD	CONVIS	ELEVAT	NATCON	NATQUA
NATSUR	NOBJNM	OBJNAM	VERACC	VERDAT	INFORM	NINFOM

For example:
SLOGRD may be used at large scale to indicate the horizontal extent of the cliff.
SLOTOP should be used on its own to encode cliffs at small scale, or in conjunction with SLOGRD to indicate the crest line of the cliff:
- when it is useful to know its elevation,
- to encode a cliff on land distant from the coastline.

Remarks:
When the cliff is coincident with the coastline, a COALNE object, with attribute CATCOA = 1 (steep coast) should be encoded, and there should be no SLOTOP or SLOGRD encoded.

### 4.7.6 Rivers (see M4 - §353)

If it is required to encode a river, it must be done using the object class RIVERS.

Geo object:	River (RIVERS)
Attributes:	NOBJNM	OBJNAM
STATUS -	5 - intermittent
INFORM	NINFOM
Remarks:
- If the river is navigable at compilation scale, it must be encoded using the object classes DEPARE or DRGARE (see clause 5.4.8), and the river banks must be encoded using the object classes COALNE or SLCONS. The river must not be encoded as a RIVERS object. If it is required to encode the name of the river, it must be done using a SEAARE object with attribute CATSEA = 53 (river).
- If it is required to encode a river that is not navigable at compilation scale, it must be done using RIVERS, covered by a LNDARE or UNSARE object. The name of the river should be encoded using the attribute OBJNAM on the RIVERS object.
- Use of the object class RIVBNK is prohibited.

### 4.7.7 Rapids, waterfalls (see M4 - §353.5)
#### 4.7.7.1 Rapids

If it is required to encode rapids within a river, it must be done using the object class RAPIDS.

Geo object:	Rapids (RAPIDS)
Attributes:	NOBJNM	OBJNAM	VERACC	VERLEN	INFORM	NINFOM

The area covered by rapids must also be covered by a RIVERS object, and a LNDARE or UNSARE object.

#### 4.7.7.2 Waterfalls

If it is required to encode a waterfall within a river, it must be done using the object class WATFAL.

Geo object:	Waterfall (WATFAL)
Attributes:	CONVIS	NOBJNM	OBJNAM	VERACC	VERLEN	INFORM	NINFOM

The area covered by a waterfall must also be covered by a RIVERS object, and a LNDARE or UNSARE object.
### 4.7.8 Lakes (see M4 - §353.6)

If it is required to encode a lake, it must be done using the object class LAKARE.

Geo object:	Lake (LAKARE)
Attributes:	ELEVAT	NOBJNM	OBJNAM	VERACC	VERDAT	INFORM	NINFOM

Remarks:
- If the lake is navigable at compilation scale, it must be encoded using the object classes DEPARE or DRGARE (see clause 5.4.8), and the lake shore must be encoded using the object classes COALNE or SLCONS. The lake must not be encoded as a LAKARE object. If it is required to encode the name of the lake, it must be done using a SEAARE object, with attribute CATSEA = 52 (lake).
- If it is required to encode a lake that is not navigable at compilation scale, it must be done using LAKARE, covered by a LNDARE or UNSARE object. The name of the lake should be encoded using the attribute OBJNAM on the LAKARE object.
- Use of the object class LAKSHR is prohibited.
### 4.7.9 Saltpans (see M4 - §353.7)

If it is required to encode a saltpan area, it must be done using a LNDRGN object, with attribute CATLND = 15 (salt pan) covered by a LNDARE object (i.e. the saltpan does not form a hole in the land area).

If the seaward edge of an encoded saltpan area is coincident with the coastline, it should be encoded using a COALNE object, with attribute CATCOA = 2 (flat coast).

### 4.7.10 Glaciers (see M4 - §353.8)

If it is required to encode the portion of a glacier that is on land, it must be done using an ICEARE object, with attribute CATICE = 5 (glacier) covered by a LNDARE object (i.e. the glacier does not form a hole in the land area).

If the seaward edge of an encoded glacier is coincident with the coastline, this edge should be encoded using a COALNE object, with attribute CATCOA = 6 (glacier (seaward end)).

ICEARE objects that are located in the sea must be covered by a LNDARE or UNSARE object, if the depth of water beneath them is unknown, or covered by a DEPARE object, if the depth is known.

### 4.7.11 Vegetation (see M4 - §312.4, §352.4 and §354)

If it is required to encode vegetation, it must be done using the object class VEGATN.

Geo object:	Vegetation (VEGATN)
Attributes:	CATVEG	CONVIS	ELEVAT
HEIGHT -	approximate altitude of the highest point of the top of the vegetation
NOBJNM	OBJNAM	VERACC	VERDAT	VERLEN	INFORM	NINFOM

If it is required to encode an isolated tree used as a landmark, it must be done using a VEGATN object, with attribute CATVEG = 13 to 21.

If it is required to encode a mangrove area, it must be done using a VEGATN object, with CATVEG = 7 (mangroves).

The seaward edge of an encoded mangrove area should be encoded using a COALNE object, with attribute CATCOA = 7 (mangrove), and the mangrove area’s spatial object should have the attribute QUAPOS = 4 (approximate).

### 4.7.12 Lava flow (see M4 - §355)

If it is required to encode a lava flow, it must be done using a LNDRGN object, with attribute CATLND = 14 (lava flow).

## 4.8 Artificial features

### 4.8.1 Canals (see M4 - §361)

If it is required to encode a canal, it must be done using the object class CANALS.

Geo object:	Canal (CANALS)
Attributes:	CATCAN	CONDTN	DATEND	DATSTA
HORACC -	applies only to HORCLR
HORCLR	HORWID	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

Remarks:
- If the canal is navigable at compilation scale, it must be encoded using the object classes DEPARE or DRGARE (see clause 5.4.8), and the canal banks must be encoded using the object classes COALNE or SLCONS. The canal must not be encoded as a CANALS object. If it is required to encode the name of the canal, it must be done using a SEAARE object, with attribute CATSEA = 51 (canal).
- If it is required to encode a canal that is not navigable at compilation scale, it must be done using CANALS, covered by a LNDARE or UNSARE object. The name of the canal should be encoded using the attribute OBJNAM on the CANALS object.
- Use of the object class CANBNK is prohibited.

### 4.8.2 Railways (see M4 - §362)

If it is required to encode a railway, it must be done using the object class RAILWY.

Geo object:	Railway (RAILWY)
Attributes:	CONDTN	HEIGHT	NOBJNM	OBJNAM	STATUS	VERACC	INFORM	NINFOM

Remarks:
If it is required to encode a railway station, it must be done using a BUISGL object, with attribute FUNCTN = 8 (railway station).

### 4.8.3 Tunnels (see M4 - §363.1)

If it is required to encode a tunnel, it must be done using the object class TUNNEL.

Geo object:	Tunnel (TUNNEL)
Attributes:	BURDEP	CONDTN
HORACC -	applies only to HORCLR
HORCLR	NOBJNM	OBJNAM
VERACC	-	applies only to VERCLR
VERCLR	STATUS
INFORM	NINFOM

Remarks:
- If there is a waterway inside the tunnel, and the waterway is navigable at compilation scale, it must be encoded as if it were a navigable canal (see clause 4.8.1), using the object classes DEPARE or DRGARE in conjunction with the TUNNEL object. There must be no LNDARE object in the area covering the waterway.
- If it is required to encode a waterway inside a tunnel that is not navigable at compilation scale, it must be done using the object class CANALS in conjunction with the TUNNEL object. A LNDARE object must cover the tunnel. The attributes HORACC, HORCLR, VERACC and VERCLR must not be encoded on the TUNNEL object in this case.
- If it is required to encode a tunnel that has no waterway inside it (but a railway, road etc), only the TUNNEL object must be encoded (not the railway or the road), covered by LNDARE, DEPARE, DRGARE or UNSARE objects as appropriate.

### 4.8.4 Cuttings and embankments (see M4 - §363.2 and §364.1)

If it is required to encode cuttings and embankments, this must be done in the same way as cliffs; using SLOGRD and / or SLOTOP objects (see clause 4.7.5), with attribute CATSLO = 1 (cutting) or 2 (embankment).

### 4.8.5 Dams (see M4 - §364.2)

If it is required to encode a dam, it must be done using the object class DAMCON.

Geo object:	Dam (DAMCON)
Attributes:	CATDAM	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA	HEIGHT	NATCON	NOBJNM	OBJNAM	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
- When a DAMCON object is of type area, it must be covered by a LNDARE object.
- The geometry of the dam includes any gates. Gates should be encoded as separate GATCON objects.

### 4.8.6 Flood barrages (see M4 - §326.7)

If it is required to encode the fixed part of a flood barrage, and the flood barrage is inside an area which is navigable at compilation scale, it must be done using a DAMCON object, with attribute CATDAM = 3 (flood barrage), and must be covered by a LNDARE object . If it is required to encode the opening part of the flood barrage, it must be done using a GATCON object, with attribute CATGAT = 2 (flood barrage gate), and must be covered by a DEPARE object .

When an encoded flood barrage is inside an area that is not navigable at compilation scale, the gates need not be encoded. In this case, the DAMCON object must go all the way across the river or lake.

### 4.8.7 Dykes (see M4 - §313.1)

If it is required to encode a dyke, it must be done using the object class DYKCON.

Geo object:	Dyke (DYKCON)
Attributes:	CONDTN	CONRAD	DATEND	DATSTA	HEIGHT	NATCON	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
- If it is required to encode a dyke whose seaward edge is coincident with the coastline, it must be done using DYKCON, and with a SLCONS object of type line along its seaward edge, with no value populated for attribute CATSLC.
- When a DYKCON object is of type area, it must be covered by a LNDARE object.
- At large compilation scales, the dyke crown (the topline of the dyke) may be encoded as a SLOTOP object, with attribute CATSLO = 2 (embankment).
### 4.8.8 Roads and tracks (see M4 - §365)

If it is required to encode a road or track, it must be done using the object class ROADWY.

Geo object:	Road (ROADWY)
Attributes:	CATROD	CONDTN	NATCON	NOBJNM	OBJNAM	STATUS	INFORM
NINFOM

Remarks:
Road crossings (attribute CATROD = 7) should not be encoded.

### 4.8.9 Causeways

If it is required to encode a causeway, it must be done using the object class CAUSWY.

Geo object:	Causeway (CAUSWY)
Attributes:	CONDTN	NATCON	NOBJNM	OBJNAM	STATUS	WATLEV	INFORM
NINFOM

### 4.8.10 Bridges (see M4 - §381)

If it is required to encode a bridge, it must be done using the object class BRIDGE.

Geo object:	Bridge (BRIDGE)
Attributes:	CATBRG -	mandatory over navigable waters
COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND
DATSTA
HORACC -	applies only to HORCLR
HORCLR	NATCON	NOBJNM	OBJNAM
VERACC -	applies only to VERCCL, VERCLR, VERCOP
VERCCL -	mandatory for opening bridges
VERCLR -	mandatory for non-opening bridges
VERCOP -	mandatory for opening bridges with limited clearance
VERDAT -	applies only to VERCCL, VERCLR, VERCOP
INFORM	NINFOM

Remarks:
- Water under a bridge must be encoded using the object class DEPCNT and the object classes DEPARE, DRGARE or UNSARE if the waterway is navigable at compilation scale, or using the object classes LNDARE or UNSARE if the waterway is not navigable at compilation scale.
- In navigable water, bridge supports must be encoded, where possible, using a PYLONS object (see clause 4.8.18), with attribute CATPYL = 4 or 5.
- It is not mandatory to encode roads or railways on bridges.

### 4.8.11 Conveyors (see M4 - §382.3)
###
If it is required to encode a conveyor, it must be done using the object class CONVYR.

Geo object:	Conveyor (CONVYR)
Attributes:	CATCON	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND
DATSTA	HEIGHT	LIFCAP	NOBJNM	OBJNAM	PRODCT	STATUS
VERACC -	applies only to VERCLR (not HEIGHT)
VERCLR -	mandatory over navigable waters
VERDAT -	applies only to VERCLR (not HEIGHT)
VERLEN	INFORM	NINFOM

### 4.8.12 Airfields (see M4 - §366)

At large scale, an airport should be encoded using a combination of the following objects: AIRARE (area), RUNWAY (area or line), BUISGL (area or point) and LNDMRK (area or point). At least one AIRARE or RUNWAY must be in this set of objects. Where it is necessary to establish a relationship between these objects, they should be associated using the collection object C_ASSO (see clause 15).

At small scale, an airport should be encoded as an AIRARE of type point.

Geo object:	Airport / airfield (AIRARE)
Attributes:	CATAIR	CONDTN	CONVIS	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

Geo object:	Runway (RUNWAY)
Attributes:	CATRUN	CONDTN	CONVIS	NATCON	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM	NINFOM

Remarks:
- If individual buildings are visually conspicuous, they must be encoded as separate objects.
- Two or more crossing runways may be encoded as one area.
- If it is required to encode the control tower, it must be done using a LNDMRK object, with attributes FUNCTN = 39 (control) and CATLMK = 17 (tower). If it is required to encode other buildings, this must be done using the object class BUISGL.
- If it is required to encode a seaplane landing area, it must be done using the object class SPLARE (see clause 11.12).

### 4.8.13 Production and storage areas (see M4 - §367)

If it is required to encode production or storage area, it must be done using the object class PRDARE.

Geo object:	Production / storage area (PRDARE)
Attributes:	CATPRA	CONDTN	CONRAD	CONVIS	DATEND	DATSTA
ELEVAT	HEIGHT	NOBJNM	OBJNAM	PRODCT	STATUS	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
- It there are individual buildings or equipment objects contained within this area, they should be encoded as separate objects such as BUISGL, CRANES, LNDMRK or SILTNK within the PRDARE area object.
- If visible from seaward, a quarry face should be encoded in a similar way to a cliff (see clause 4.7.5), with attribute CATSLO = 6 (cliff).

### 4.8.14 Built-up areas (see M4 - §370)

If it is required to encode a built-up area, it must be done using the object class BUAARE.

Geo object:	Built-up area (BUAARE)
Attributes:	CATBUA	CONDTN	CONRAD	CONVIS	HEIGHT	NOBJNM	OBJNAM
VERACC	VERDAT	INFORM	NINFOM

Remarks:
- A built-up area crossed by line objects (e.g. roads, streets, railways) should not be divided into multiple objects, unless separate sections of the built-up area have at least one different attribute value.
- However, for presentation purposes, a built up area of type area crossed by a river or canal of type area must be divided into several objects, with the built-up area objects not overlapping the river or canal object. A built up area of type area should not overlap a lake, dock or lock basin object of type area.
- Use of the object class SQUARE is prohibited.
- Several buildings or built-up areas may be referred to by the same settlement, village or town name on the source. In such cases, the individual buildings or built-up areas should be encoded as separate unnamed objects, using the object classes BUISGL or BUAARE, and additionally, an ADMARE object (see clause 14) covering the whole named area should be created with the name encoded using the attribute OBJNAM. The encoded ADMARE object should also have the attribute JRSDTN = 3 (national sub-division).

### 4.8.15 Buildings, landmarks, tanks, silos (see M4 - §370 to §378)

If it is required to encode buildings, landmarks, tanks or silos, they must be done using the object classes BUISGL, LNDMRK or SILTNK, depending on their shape and use. The following table describes the way to encode these objects.

Geo object:	Building, single (BUISGL)
Attributes:	BUISHP	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	ELEVAT
FUNCTN	HEIGHT	NATCON	NOBJNM	OBJNAM	STATUS	VERACC
VERDAT	VERLEN	INFORM	NINFOM

Geo object:	Landmark (LNDMRK)
Attributes:	CATLMK	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	ELEVAT
HEIGHT	NATCON	NOBJNM	OBJNAM	STATUS	FUNCTN	VERACC
VERDAT	VERLEN	INFORM	NINFOM

Geo object:	Silo / tank (SILTNK)
Attributes:	BUISHP	CATSIL	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS
ELEVAT	HEIGHT	NATCON	NOBJNM	OBJNAM	PRODCT	STATUS
VERACC	VERDAT	VERLEN	INFORM	NINFOM

In the following table, the symbol ‘/’ indicates that this attribute does not exist for that particular object class. A blank indicates that the encoder may choose a relevant value for the attribute. The table contains the most common examples of coding; other coding combinations are possible.

Feature	INT1	Object-class	FUNCTN	CATLMK	BUISHP	PRODCT	CATSIL
Administrative	IG72	BUISGL	18	/		/	/
Bank office		BUISGL	13	/		/	/
Buddhist temple	IE16	BUISGL	25	/		/	/
Bus station		BUISGL	42	/		/	/
Cairn	IQ100	LNDMRK	/	1	/	/	/
Cemetery	IE19	LNDMRK		2	/	/	/
Chapel	IE11	BUISGL	21	/		/	/
Chimney	IE22	LNDMRK		3		/
Church	IE10.1	BUISGL	20	/		/	/
Church dome, Cupola	IE10.4	LNDMRK	20	15	/	/	/
Church spire	IE10.3	LNDMRK	20	20	/	/	/
Church tower	IE10.2	LNDMRK	20	17	/	/	/
Clock tower		LNDMRK	38	17	/	/	/
Column	IG66	LNDMRK	/	10	/	/	/
Communication mast		LNDMRK	29	7	/	/	/
Communication tower		LNDMRK	29	17	/	/	/
Control tower		LNDMRK	39	17	/	/	/
Cooling tower		LNDMRK	35	17	/	/	/
Cross, Calvary	IE12	LNDMRK		14	/	/	/
Custom office	IF61	BUISGL	3	/		/	/
Dish aerial	IE31	LNDMRK		4	/	/	/
Dome or cupola, part of a building		LNDMRK		15	/	/	/
Educational facility		BUISGL	19	/		/	/
Factory	IG80	BUISGL	16	/		/	/
Flagstaff, Flagpole	IE27	LNDMRK		5	/	/	/
Flare stack	IE23	LNDMRK		6	/	/	/
Grain elevator		SILTNK	/	/		22	3
Harbour-master’s office	IF60	BUISGL	2	/		/	/
Headquarters for district control		BUISGL	14	/		/	/
Health office	IF62.1	BUISGL	4	/		/	/
Hospital	IF62.2	BUISGL	5	/		/	/
Hotel	ID6	BUISGL	7	/		/	/
House, Building	IG63	BUISGL		/		/	/
Large rock or boulder on land		LNDMRK	/	21	/	/	/
Light house (tower)	IP1	LNDMRK	33	17	/	/	/
Light house (other shapes)	IP1	BUISGL	33	/		/	/
Lookout station in general	IG77	BUISGL	28	/		/	/
Lookout tower		LNDMRK	28	17	/	/	/
Marabout	IE18	BUISGL	27	/		/	/
Mast in general	IG67	LNDMRK		7	/	/	/
Memorial plaque		LNDMRK		11	/	/	/
Microwave tower		LNDMRK	34	17	/	/	/
Minaret	IE17	LNDMRK	26	20	/	/	/
Monument	IE24	LNDMRK		9	/	/	/
Mooring mast	IG69	LNDMRK	40	7	/	/	/
Mosque	IE17	BUISGL	26	/		/	/
Obelisk		LNDMRK	/	12	/	/	/
Observation tower		LNDMRK	36	17	/	/	/
Pagoda	IE14	BUISGL	23	/		/	/
Pilot lookout	IT2	BUISGL	12	/		/	/
Pilot office	IT3	BUISGL	11	/		/	/
Police station		BUISGL	9	/		/	/
Post office	IF63	BUISGL	6	/		/	/
Power station	IG88	BUISGL	17	/		/	/
Radar dome	IE30.4	LNDMRK	32	15	/	/	/
Radar mast	IE30.1	LNDMRK	32	7	/	/	/
Radar scanner	IE30.3	LNDMRK		16	/	/	/
Radar tower	IE30.2	LNDMRK	32	17	/	/	/
Radio mast	IE28	LNDMRK	31	7	/	/	/
Radio tower	IE29	LNDMRK	31	17	/	/	/
Railway station	ID13	BUISGL	8	/		/	/
Shinto shrine	IE15	BUISGL	24	/		/	/
Silo	IE33	SILTNK	/	/			1
Spire, part of a building		LNDMRK		20	/	/	/
Stadium		BUISGL	41	/		/	/
Statue		LNDMRK		13	/	/	/
Tank	IE32	SILTNK	/	/			2
Television mast	IE28	LNDMRK	30	7	/	/	/
Television tower	IE29	LNDMRK	30	17	/	/	/
Temple	IE13	BUISGL	22	/		/	/
Timeball tower		LNDMRK	37	17	/	/	/
Tower	IE20	LNDMRK		17	/	/	/
Tower, part of a building		LNDMRK		17	/	/	/
Transit shed, Warehouse	IF51	BUISGL	15	/		/	/
Water tower	IE21	SILTNK	/	/	/	3 or 8	4
Water-police station		BUISGL	10	/		/	/
Windmill	IE25	LNDMRK		18	/	/	/
Windmotor	IE26	LNDMRK		19	/	/	/
						table 4.1

Remarks:
- A ruined building or landmark should be encoded in the same way as the feature in good condition, but with attribute CONDTN = 2 (ruined).
- When a building is shown as an area, indicating its true shape, and it is required to encode a prominent feature such as a tower or spire that is part of the structure, two objects must be created (see Figure 3 b):
a BUISGL object of type area for the main building,
-	a LNDMRK object of type point for the prominent feature.
Not all landmarks are visually conspicuous. If a feature is visually conspicuous (i.e. it is distinctly and noticeably visible from seaward), the attribute CONVIS = 1 (visually conspicuous) must be encoded (see M-4 §340).

Figure 3 - Landmarks
### 4.8.16 Fences and walls

If it is required to encode a fence or wall, it must be done using the object class FNCLNE.

Geo object:	Fence/wall (FNCLNE)
Attributes:	CATFNC	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS
ELEVAT	HEIGHT	NATCON	NOBJNM	OBJNAM	STATUS
VERACC	VERDAT	VERLEN	INFORM	NINFOM

### 4.8.17 Fortified structures (see M4 - §379)

If it is required to encode a fortified structure, it must be done using the object class FORSTC.

Geo object:	Fortified structure (FORSTC)
Attributes:	CATFOR	CONDTN	CONRAD	CONVIS	HEIGHT	NATCON	NOBJNM	OBJNAM	VERACC	VERDAT	VERLEN	INFORM	NINFOM

### 4.8.18 Pylons and bridge supports (see M4 - §381 and §382)

If it is required to encode a pylon or bridge support, it must be done using the object class PYLONS.

Geo object:	Pylon / bridge support (PYLONS)
Attributes:	CATPYL	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA	HEIGHT	NATCON	NOBJNM	OBJNAM	VERACC	VERDAT	VERLEN	WATLEV	INFORM	NINFOM

Remarks:
A PYLONS object of type area with attribute WATLEV = 1,2 or 6 must be covered by a LNDARE object of type area (see clause 4.8.10).

### 4.8.19 Oil barriers

If it is required to encode an oil barrier, it must be done using the object class OILBAR.

Geo object:	Oil barrier (OILBAR)
Attributes:	CATOLB	CONDTN	DATEND	DATSTA	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

### 4.8.20 Views and sketches, viewpoints

If it is required to indicate a drawing or a photograph, the attribute PICREP must be used to indicate the file name (without the path) of the external graphical file. Picture files that form part of the ENC must be in TIFF format. Picture files in other formats may be used if a private agreement exists between the producing authority and receiver. An ECDIS may not be able to display files in formats other than TIFF.

### 4.8.21 Signs and Notice boards

If it is required to encode a fixed or floating sign or notice board, it must be done using a BCNSPP object (see clause 12.3.1) or BOYSPP object (see clause 12.4.1), with attribute CATSPM = 18 (notice mark), or using the object class DAYMAR (see clause 12.3.3).

Remarks:
- If it is required to encode a sign or notice board that has more than one colour, the attributes COLOUR and COLPAT must be used, according to the rules laid out in clause 2.4.
- If it is required to encode any text shown on a notice board or sign, it must be done using the attribute INFORM.
- If it is required to encode the shape and colour of a notice board, it must be done by encoding the board as a DAYMAR object.
# 5. Depth

Figure 4 – Depth contours
## 5.1 Sounding datum

See clause 2.1.3.

## 5.2 Depth contours (see M4 - §411)

Geo object:	Depth contour (DEPCNT)
Attributes:	VALDCO -	value of depth contour (negative value for drying contours)
VERDAT	INFORM	NINFOM

The boundary of a drying rocky area (see INT1 ‑ IJ20) or coral reef (see INT1 ‑ IJ22) may be coincident with the zero metre contour (see ‘fg’ in Figure 4). If it is required to encode this boundary, it must be done using the object class DEPCNT with the attribute VALDCO = 0.

On paper charts, the presentation of contours in areas of steep slope is sometimes generalised so that closely spaced contours are removed to leave a single contour (see ‘ab’ in Figure 4). In such cases, this contour must be encoded using the shallowest depth of the slope. A linear depth area must also be created at the same position (see clause 5.4.3).

Wherever possible, contours must be closed, or connected to the border of the cell, a coastline feature or another contour, in order to define closed areas.

Spatial objects associated with approximate contours should be encoded using the attribute QUAPOS = 4 (approximate).

## 5.3 Soundings (see M4 - §412)

Geo object:	Sounding (SOUNDG)
Attributes:	EXPSOU -	indicates objects with a “value of sounding” within or not within the range of depth of the surrounding area
NOBJNM	OBJNAM
QUASOU -	see Table 5.1 below
SOUACC -	see use of the meta object M_QUAL (clauses 2.2.3.1 and 2.2.3.4)
STATUS -	18 - existence doubtful
TECSOU -	only for lower reliability soundings
VERDAT	INFORM	NINFOM
SORDAT -	see Table 5.1 below

Sounding	M4	INT 1	QUAPOS	QUASOU	Remarks
In true position	412.1	II10		1	Should be encoded using QUAPOS = 10
Out of position / on paper chart	412.2	II11 / II12		1	Spatial object must be encoded at the true position. There is no “sounding, out of position” in an ENC.
No bottom found	412.3	II13		5
Lower reliability	412.4	II14	4	4
Drying	413	II15		1	Negative value
Doubtful	424.4	II2		3	Existence doubtful should be encoded using STATUS = 18
Reported but not confirmed		II4	8	9	If available, the year of report must be encoded using the attribute SORDAT
					table 5.1

A sounding associated with a rock or coral pinnacle which is an obstruction to navigation must be encoded using the object class UWTROC (INT1 IK14) with attribute VALSOU populated with the value of the sounding.

The geometry of soundings is held in a 3 dimensional array (latitude, longitude, depth). In the interests of efficiency, multiple soundings should be encoded in one spatial object, provided that all the spatial and geo object attributes are common to the group.

As the sounding multiplication factor (SOMF) for ENC is always 10, soundings must only be encoded to one decimal place of a metre. Drying soundings must be indicated by a negative value.

For soundings surrounded by a danger line, see clause 6.3.

## 5.4 Depth areas

### 5.4.1 Geo object depth areas

The sea area, the intertidal area and the navigable parts of rivers, lakes and canals must be divided into depth areas, each of them having a range of depth.

As many depth areas as possible must be created using encoded depth contours.

In the maritime area, there may be a discontinuity in the succession of minimum and maximum depths of adjoining Group 1 area objects (e.g. attributes DRVAL1 and DRVAL2 for DEPARE and DRGARE objects, or height of the coastline (-H) for other Group 1 objects). If this occurs, a DEPARE object of type line must be created to fill this gap.

DEPARE objects of type line are used to ensure the continuity of the line making up the safety contour on an ECDIS, taking into account the requirement of S-52 that a safety contour should be displayed to enable the mariner to clearly see the dividing line between safe and unsafe water.

A DEPARE object of type line must be encoded where two or more of the contours in a data set merge to form a single “cliff contour”. This may happen naturally, or at a dredged area boundary, at a coastline or shoreline construction, etc. However, a DEPARE object of type line may also be created at the borders of area objects DEPARE and DRGARE when there is no discontinuity in the succession of their minimum and maximum depths, and the limit between the two objects does not contain any COALNE, DAMCON, DEPCNT, GATCON, LNDARE or SLCONS objects of type line.

A DEPARE object of type line may also be created at the borders of FLODOC, HULKES, PONTON, UNSARE and LNDARE objects of type area. In all such cases, the DRVAL1 of the DEPARE line objects should be set to -H (see definition of H in Figure 6 below).

DEPARE objects of type area are part of Group 1.

Geo object:	Depth area (DEPARE)
Attributes:	DRVAL1 -	(see clause 5.4.3)
DRVAL2 -	(see clause 5.4.3)
QUASOU	SOUACC	VERDAT	INFORM	NINFOM

### Geometry of depth areas

Where areas are not closed on the source, it may be necessary to close these areas using edges without associated line objects. This is mandatory at the boundary of a cell (see Figure 5).

Remarks:

Figure 5 – Geometry of depth areas
For short isolated sections of DEPCNT objects such as (bc), it is up to the producing authority whether to encode the small area (abcda) as a separate DEPARE object of type area, or to encode only the line (bc) as a floating DEPCNT object.

### 5.4.3 Use of attributes DRVAL1 and DRVAL2 for depth areas in general

For each depth area of type area, DRVAL1 and DRVAL2 should be encoded with the values corresponding to the shallowest and deepest depths in that area. These values, except for the shallowest and deepest areas, should be chosen from the values of the depth contours encoded in the data set.

The overall succession of DRVAL1 and DRVAL2 in the whole maritime area should be continuous (no gaps, no overlaps). Therefore, for each DEPARE object of type line, DRVAL1 usually takes the maximum value (DRVAL2) of the shallowest adjoining Group 1 DEPARE or DRGARE area object, and DRVAL2 takes the minimum value (DRVAL1) of the deepest adjoining DEPARE or DRGARE area object. However, in some cases DRVAL1 and DRVAL2 may be set to the same value, dependent upon the information shown on the source data. Also, if the shallowest adjoining Group 1 area is a FLODOC, HULKES, LNDARE, PONTON or UNSARE object of type area, the DRVAL1 value of the DEPARE line object, if required, should be set to -H (see definition of H in Figure 6 below).

A drying area, within which a drying height is indicated without a true position, should be encoded using a DEPARE object, with DRVAL1 usually set to -H and DRVAL2 set to a data set contour value (usually zero). The drying height should be encoded using the attribute INFORM on the DEPARE object (e.g. Dries 1.4).

Figure 6 – Depth areas

(a): H = Height of the coastline datum above sounding datum, or a rounded value (e.g. (1) the value of the highest drying contour indicated on the source document; (2) zero, if the coastline datum is the same as the sounding datum).

In the following clauses, the paragraph numbers refer to the item numbers in Figure 6. These clauses do not cover all encoding scenarios and must be used in conjunction with the clauses associated with Figure 7 in clause 5.4.4 below.

1.	If the depth area is bounded by two or more depth contours:
DRVAL1 should take the value of the data set depth contour immediately shallower than the value of DRVAL2.
DRVAL2 should take the value of the deepest depth contour bounding the area.

If the deepest depth is shown by a depth contour, and the shallowest depth is shown by a sounding (a shoal):
DRVAL1 should take the value of the data set depth contour immediately shallower than the value of the sounding or ‑H.
DRVAL2 should take the value of the depth contour.
3.	If the deepest depth is shown by a sounding and the shallowest depth is shown by a depth contour (a deep):
DRVAL1 should take the value of the depth contour.
DRVAL2 should take the value of the data set depth contour immediately deeper than or equal to the value of the sounding.

4.	If the shallowest depth is defined by the coastline:
DRVAL1 should take the value of -H.
DRVAL2 should take the value of the shallowest data set depth contour bounding the area.

5.	If the depth area is bounded by only one depth contour, contains no soundings, and is a shoal:
DRVAL1 should take the value of the data set depth contour immediately shallower than the value of the depth contour, or -H.
DRVAL2 should take the value of the depth contour.

6.	If the depth area is bounded by only one depth contour, contains no soundings, and is a deep:
DRVAL1 should take the value of the depth contour.
DRVAL2 should take the value of the data set depth contour immediately deeper than the value of the depth contour.

7.	If two or more depth contours are merged (a cliff), a DEPARE object of type line must be created at the same position:
DRVAL1 should take the value of the DRVAL2 of the shallowest DEPARE area object sharing the cliff as its boundary.
DRVAL2 should take the value of the deepest of the merged depth contours.

8.	If one or more depth contours are merged with the coastline, a DEPARE object of type line must be created at the same position:
DRVAL1 should take the value of -H.
DRVAL2 should take the value of the DRVAL1 of the DEPARE area object for which the section of coastline forms the boundary.

9.	If the depth area is bounded by an incomplete depth contour on one side (such as in incompletely surveyed area), and a complete depth contour on the other:
If encoded, DRVAL1 should take the value of the shallowest depth contour.
If encoded, DRVAL2 should take the value of the deepest depth contour.
Note: The encoding of this DEPARE object as a separate area is optional - see also Figure 5.

10.	If the depth area is bounded by complete depth contours, but contains an incomplete (floating) depth contour:
DRVAL1 should take the value of the shallowest depth contour.
DRVAL2 should take the value of the deepest depth contour.

### 5.4.4 Use of attributes DRVAL1 and DRVAL2 for depth areas adjoining non-navigable waterways

Figure 7 – Depth areas at seaward end of a non-navigable waterway and approaches
Remarks:
The DEPARE line objects (ab), (bd) and (de) should be encoded as a single linear feature object (abde).

In the following clauses, the paragraph numbers refer to the item numbers in Figure 7. These clauses do not cover all encoding scenarios and must be used in conjunction with the clauses associated with Figure 6 in clause 5.4.3 above.

1.	If a depth area is intertidal and adjacent to a non-navigable waterway (RIVERS, CANALS or DOCARE object):
DRVAL1 should take the value of -H.
DRVAL2 should take the value of the deepest depth contour bounding the area (normally zero).

2.	If a depth area is always under water and adjacent to a non-navigable waterway (RIVERS, CANALS or DOCARE object):
DRVAL1 should take the value of the shallowest depth contour bounding the area, or the DRVAL2 of a DEPARE line object sharing the contour, if it exists.
DRVAL2 should take the value of the deepest depth contour bounding the area.

3.	If a depth area is always under water and adjacent to a non-navigable waterway, a DEPARE object of type line should be created to close the non-navigable waterway. This border of the waterway may also be encoded as a masked line:
DRVAL1 should take the value of -H.
DRVAL2 should take the value of the DRVAL1 of the adjoining depth area.

4.	If one or more depth contours merge with the coastline to form a cliff, a DEPARE object of type line should be created at the same position as the cliff:
DRVAL1 should take the value of -H.
DRVAL2 should take the value of DRVAL1 of the area DEPARE object for which the section of coastline forms part of the boundary.

5.	If it is required to encode non-navigable waterways, they must be done using the object classes CANALS, DOCARE or RIVERS, and must be covered by LNDARE or UNSARE objects of type area.

### 5.4.5 Use of attributes DRVAL1 and DRVAL2 for depth areas adjoining constructions which are always dry

Figure 8 – Depth areas adjoining a shoreline construction

### 5.4.6 Use of attributes DRVAL1 and DRVAL2 for depth areas adjoining a dredged area

Figure 9 – Depth areas adjoining a dredged area

When a dredged area has a depth of dredging which is deeper than the DRVAL2 of adjoining Group 1 area objects (DEPARE), the boundary of the dredged area must be encoded as a series of DEPARE objects of type line between each intersection with a depth contour:
DRVAL1 should take the value of the maximum depth (DRVAL2) of the adjoining Group 1 area object, or -H.
DRVAL2 should take the value of the depth of dredging.
### 5.4.7 Use of attributes DRVAL1 and DRVAL2 for dredged areas adjoining dredged areas

In Figure 10, the following DEPARE objects of type line must be encoded, with the following attribute values (see clause 5.4.6):

Figure 10 – Dredged areas adjoining dredged areas

(ab)	DRVAL1 =	10	DRVAL2 =	12
(cd)	DRVAL1 =	5	DRVAL2 =	8.6
(de)	DRVAL1 =	5	DRVAL2 =	9
(fg)	DRVAL1 =	5	DRVAL2 =	8.6
(hi)	DRVAL1 =	10	DRVAL2 =	12

When the depth of dredging is within the range of depths of the adjoining depth area, there should be no geo feature object of type line encoded on the boundary (i.e (bc), (ei), (fh) in Figure 10).

When two dredged areas adjoin:
If the depths of dredging of the two adjoining dredged areas are either side of one or more data set depth contour intervals, the boundary must be encoded as a DEPARE object of type line:
DRVAL1 should take the value of the depth of dredging of the shallower dredged area.
DRVAL2 should take the value of the depth of dredging of the deeper dredged area.

In Figure 10, this corresponds to the following boundaries:

(bj)	DRVAL1 =	8.6	DRVAL2 =	12
(ij)	DRVAL1 =	9	DRVAL2 =	12
(hk)	DRVAL1 =	8.6	DRVAL2 =	12

If the depths of two adjoining dredged areas fall within a data set depth contour interval, there should be no geo feature object of type line encoded on the boundary (i.e. (dj) in Figure 10).

Figure 11 – Linear depth areas along dredged area boundaries
In Figure 11, the 5 metre dredged area extends into the 5-10 metre depth area. In order to ensure that the safety contour can be drawn correctly, linear depth areas ((bc) and (ah)) must be created with both DRVAL1 and DRVAL2 set to 5 metres along these sections of the boundary of the dredged area. There should be no linear depth areas between (ge) and (cd).

### 5.4.8 Rivers, canals, lakes, basins

Where these areas are navigable at compilation scale, they must be encoded using the Group 1 object classes DEPARE, DRGARE or UNSARE, and coastline-type object classes COALNE or SLCONS. If it is required to encode the nature and name of the area, it must be done using the object class SEAARE.

Where these areas are required and are not navigable at compilation scale, they must be encoded using the object classes RIVERS, CANALS, LAKARE, DOCARE or LOKBSN. These objects must be covered by LNDARE or UNSARE objects. Use of the object classes CANBNK, LAKSHR and RIVBNK is prohibited.

## 5.5 Dredged areas (see M4 - §414)

If it is required to encode dredged areas, this must be done using the object class DRGARE.

Geo object:	Dredged area (DRGARE)
Attributes:	DRVAL1 -	depth of dredging
DRVAL2 -	depth of dredging (if different to DRVAL1)
NOBJNM	OBJNAM
QUASOU -	10 - maintained depth
11 - not regularly maintained
If encoded, the value of QUASOU must be one of the above
RESTRN
SOUACC -	see use of M_QUAL (clause 2.2.3.1)
TECSOU	VERDAT
INFORM -	date of dredging (e.g. Dredged in 1995)
NINFOM -	date of dredging in national language (e.g. Dragué en 1995)

Remarks:
- DRGARE objects of type area are part of Group 1.
- For the encoding of the boundaries of a dredged area, see clauses 5.4.6 and 5.4.7.

## 5.6 Swept areas (see M4 - §415)

If it is required to encode a swept area, it must be done using the object class SWPARE.

Geo object:	Swept area (SWPARE)
Attributes:	DRVAL1 -	swept depth
QUASOU	SOUACC
TECSOU -	6	- swept by wire-drag
8	- swept by vertical acoustic system
- swept by side scan sonar
If encoded, the value of TECSOU must be one of the above
VERDAT
INFORM -	latest date of sweeping (e.g. Swept in 1998)
NINFOM

Spot soundings and depth contours shown in these areas must be encoded using SOUNDG and DEPCNT objects. Attributes QUASOU, SOUACC and TECSOU encoded on SWPARE apply to the swept area only. When it is required to encode the quality of spot soundings and depth contours, it must be done using the meta object M_QUAL (see clause 2.2.3.1).

Even if the area contains no spot soundings or depth contours, a SWPARE object must overlap DEPARE or DRGARE objects. If there is insufficient depth information to allow the attributes DRVAL1 and DRVAL2 to be encoded on a DEPARE or DRGARE object, DRVAL1 should be set to the swept depth and DRVAL2 should be set to ‘unknown’.

Remarks:
- When a swept area occupies an entire M_QUAL area object and a SWPARE object is not defined separately, DRVAL1 for the M_QUAL object must be used to encode the swept depth. The attribute SOUACC may be used on the M_QUAL object to specify the accuracy of the swept depth defined by DRVAL1 - the attribute POSACC must not be used. There must be no depth or positional accuracy information provided for any underlying soundings within the swept area.
- When a swept area occupies an entire M_QUAL area object and a SWPARE object is defined separately, the DRVAL1 value encoded on the M_QUAL object must be the same as the DRVAL1 value encoded on the SWPARE object. SOUACC may be used on the M_QUAL object to specify the accuracy of the swept depth - POSACC must not be used. There must be no depth or positional accuracy information provided for any underlying soundings within the swept area.
- When a SWPARE object exists within a M_QUAL object, SOUACC must only be used on the M_QUAL object if the same depth accuracy applies to the swept depth and to the soundings outside the swept area. POSACC must only be used to encode the accuracy of depths falling outside the boundaries of the swept area. There must be no depth or positional accuracy information provided for any underlying soundings within the swept area.

## 5.7 Areas of continual change (see M4 - §416)

If it is required to encode an area of continually changing depth, it must be done using the object class CTNARE (see clause 6.6).

Caution notes in such areas must be encoded using the attributes INFORM or TXTDSC (see clause 6.6).

Such areas must always overlap DEPARE objects.

An area with the indication "Less water" should be encoded using this method.

If it is required to encode sand waves, they must be done using the object class SNDWAV (see clause 7.2.1).

## 5.8 Areas with inadequate depth information (see M4 - §417)

### 5.8.1 Unsurveyed areas

Areas with no bathymetric survey information, and falling within a meta object M_COVR area with attribute CATCOV = 1 (coverage available), must be encoded using the object class UNSARE.

Geo object:	Unsurveyed area (UNSARE)
Attributes:	INFORM	NINFOM

Remarks:
UNSARE objects of type area are part of Group 1.

### 5.8.2 Incompletely surveyed areas

An incompletely surveyed area should be encoded using either an UNSARE object, within which soundings and contours may be encoded (but not depth areas), or using DEPARE objects. The attributes DRVAL1 and DRVAL2 for such depth areas should have explicit values.

The area must also be covered by M_QUAL objects (see clause 2.2.3.1), with suitably defined attribute CATZOC values. Further information may be given using the meta object M_SREL, where appropriate.

A cautionary note should also be encoded using a CTNARE object of type area (see clause 6.6).
### 5.8.3 Bathymetry in areas of minimal depiction of detail on paper charts

Where areas of little or no depth information exist within a specified ENC usage, they should be encoded using one of the following options:

### 5.8.3.1 Areas of omitted bathymetry

Where larger scale coverage is available, the larger scale charts should be examined to determine the shallowest DEPARE object within the whole of the area. One DEPARE object should then be created, with attributes DRVAL1 and DRVAL2 encoded from the values obtained from the larger scale. DEPARE objects of type line may be created to join the area of omitted bathymetry with adjoining known DEPARE objects of type area.

Where larger scale coverage does not exist, a single DEPARE object should be created to cover the area of omitted bathymetry. The DRVAL1 value of the DEPARE object should be set to the shallowest value appropriate to the colour tint that is applied to it (e.g. if blue tint is used for 5-20m areas, the DRVAL1 value for the area of omitted bathymetry should be set to 5). The DRVAL2 value should be set to the shallowest value of the surrounding Group 1 polygons. DEPARE objects of type line may be created to join the area with adjoining known DEPARE objects of type area.

In either case, the areas should be covered by a CTNARE object, the boundary of which follows exactly the surrounding Group 1 objects (see clause 2.8.2).

### Areas of very simplified bathymetry

In these areas, information relating to bathymetry (e.g. depth contours, dangers, rocky areas, isolated rocks, nature of the seabed, dredged areas, unsurveyed areas) should be individually encoded as normal.

A CTNARE object should be created covering the DEPARE objects of type area, within the area of simplified bathymetry, in order to encode a cautionary note (see clause 2.8.2).

# 6. Dangers

## 6.1 Rocks and coral reefs (see M4 - §421)

### 6.1.1 Rocks which do not cover (islets)

An area feature must be encoded using:
- A LNDARE object of type area (mandatory)
- COALNE or SLCONS objects of type line (mandatory)
- LNDELV objects of type point (optional)

A line feature must be encoded using:
- A LNDARE object of type line (mandatory)
- LNDELV objects of type point (optional)

A point feature must be encoded using:
- A LNDARE object of type point (mandatory)
- A LNDELV object of type point (optional)

### 6.1.2 Rocks which may cover

These rocks may cover and uncover, may be awash, or may be always underwater.

Geo object:	Underwater / awash rock (UWTROC)
Attributes:	EXPSOU -	indicates objects with a “value of sounding” within or not within the range of depth of the surrounding area
NATQUA
NATSUR -	9 - rock
- coral
- boulder
NOBJNM	OBJNAM
QUASOU -	see Table 6.1 below.
SOUACC -	see use of the meta object M_QUAL (clause 2.2.3.1)
STATUS - 18 - existence doubtful
TECSOU
VALSOU -	see Table 6.1 below.
VERDAT
WATLEV -	see Table 6.1 below.
INFORM	NINFOM
SORDAT -	year of report, for reported but not confirmed danger

Rock or coral reef	INT 1	WATLEV	QUASOU	Comment
Covers and uncovers, depth unknown	IK11	4	2
Covers and uncovers, depth known	IK11	4	any value except 2	Negative value for VALSOU
Awash	IK12	5
Underwater rock, depth unknown	IK13	3	2
Underwater rock, depth known	IK14	3	any value except 2
Reported, not confirmed	II3.1,3.2	3,4 or 5	9	If available, the year reported should be encoded in SORDAT. / The attribute QUAPOS should be set to 8 (reported, not confirmed).
				table 6.1

Remarks:
- All UWTROC objects should be encoded using one of the above combinations of attributes.
- A rock represented by a spot sounding and an associated nature of seabed (underwater rock not dangerous to surface navigation) may be encoded using a single UWTROC object.
- For area rock features, see clause 7.1.
- When a group of rocks is surrounded by a danger line, each rock should be encoded as a separate UWTROC object covered by an obstruction area object (OBSTRN).

## 6.2 Wrecks, foul areas and obstructions (see M4 - §422)

### 6.2.1 Wrecks

If it is required to encode a wreck, it must be done using the object class WRECKS.

Geo object:	Wreck (WRECKS)
Attributes:	CATWRK -	see Table 6.2 below
CONRAD	CONVIS
EXPSOU -	indicates objects with a “value of sounding” within or not within the range of depth of the surrounding area
HEIGHT -	only if WATLEV = 1 or 2
NOBJNM	OBJNAM
QUASOU -	see Table 6.2 below
SOUACC -	see use of the meta object M_QUAL (clause 2.2.3.1)
STATUS -	13 - for historic wrecks
18 - for existence doubtful
If encoded the value of STATUS must be one of the above
TECSOU -	see Table 6.2 below
VALSOU	VERACC	VERDAT	VERLEN
WATLEV -	see Table 6.2 below
INFORM	NINFOM

In the following table, the symbol ‘/’ indicates that this attribute must not be encoded. A blank indicates that the encoder may choose a relevant value for the attribute.

Wrecks…	M4	INT 1	CATWRK	WATLEV	QUASOU	TECSOU
Showing any part of hull or superstructure	422.2	IK24 / IK20	5	1,2 or 4	/	/
Covers and uncovers	422.2	IK24 / IK21	4 or 5	4
Awash				5
The mast only is visible at high water	422.5	IK25	4 or 5	2	/	/
The mast only is visible at low water	422.5	IK25	4	4
Measured depth	422.4	IK26	1 or 2	3	6
Depth measured and swept by wire drag	422.3	IK27	1 or 2	3	6	6
Depth unknown, considered dangerous by the responsible producing authority	422.5	IK28	2	3	2	/
Depth unknown, not considered dangerous by the responsible producing authority	422.6	IK29	1	3	2	/
Depth unknown, with a safe clearance	422.7	IK30	1 or 2	3	7	/
Distributed remains of wreck	422.8	IK31	3
Reported, not confirmed	424.5	II 3.1,3.2			9
						table 6.2

All wrecks should be encoded using one of the above combinations of attributes.

Where a wreck is shown with its true shape (large scale chart):
Soundings and heights are often given inside a wreck to show the highest points of the hull or superstructure (e.g. mast, funnel). If it is required to encode such features, they must be done using:
- A WRECKS object of type area with all populated attributes applying to the highest point of the wreck.
- LNDELV objects of type point to encode the features of the wreck that are always dry; the type of each feature (e.g. mast, funnel) may be encoded using the attributes INFORM and NINFOM.
- SOUNDG objects to encode the features of wrecks which are always submerged, or cover and uncover; the type of each feature (e.g. mast, funnel) may be encoded using INFORM and NINFOM, which means that these soundings must be encoded individually.

Remarks:
- A WRECKS object of type area must be covered by an area object from Group 1 as appropriate.
- If it is required to encode a wreck whose true depth is unknown, but for which there is a safe clearance depth, it must be done using the attribute VALSOU and the attribute QUASOU = 7 (least depth unknown, safe clearance at value shown).

### 6.2.2 Obstructions and foul areas

If it is required to encode snags, stumps, wellheads, diffusers, cribs, fish havens, foul areas, foul grounds, booms, ice booms or ground tackle, it must be done using the object class OBSTRN.

Geo object:	Obstruction (OBSTRN)
Attributes:	CATOBS	CONDTN
EXPSOU -	indicates objects with a “value of sounding” within or not within the range of depth of the surrounding area
HEIGHT -	only if WATLEV = 1 or 2
NATCON	NATQUA	NATSUR	NOBJNM	OBJNAM
PRODCT -	only used for wellheads
QUASOU -	see Table 6.3 below
SOUACC -	see use of the meta object M_QUAL (clause 2.2.3.1)
STATUS -	18 - existence doubtful
TECSOU -	see Table 6.3 below
VALSOU	VERACC	VERDAT
VERLEN -	distance above the sea bed
WATLEV -	see Table 6.3 below
INFORM	NINFOM

In the following table, the symbol ‘/’ indicates that this attribute must not be encoded. A blank indicates that the encoder may choose a relevant value for the attribute.

Obstruction...	INT 1	WATLEV	QUASOU	TECSOU
Depth unknown	IK40	3 or 4	2	/
Least depth known	IK41	3 or 4	6
Swept by wire to the depth shown	IK42	3	6	6
				table 6.3

All obstructions should be encoded using one of the above combinations of attributes.

Remarks:
- If the nature of a dangerous underwater object, dangerous underwater area, or floating object is not explicitly known, it must be encoded using OBSTRN.
- An OBSTRN object of type area must be covered by an area object from Group 1 as appropriate.
- In certain circumstances where an obstruction is always dry (e.g. cribs), it may be covered by a LNDARE object.

## 6.3 Danger lines

### 6.3.1 Danger line around a point danger or an isolated sounding

In general terms, a danger line that surrounds a single symbol or sounding (e.g. INT1 - IK28, IK40a or IK 41 to IK43.1) should not be encoded as a separate area. However, when the danger line indicates the true shape of the feature, it should be encoded using WRECKS or OBSTRN objects of type area. A single sounding enclosed by a danger line should be encoded using an OBSTRN object of type point. The sounding value, in this case, must be encoded using the attribute VALSOU.

### Danger line limiting an area of wrecks or obstructions

Figure 12 – Area of wrecks

The area enclosed by the danger line must be encoded using WRECKS or OBSTRN objects of type area, with the attribute values, when encoded, reflecting the characteristics of the shallowest point object encoded in the area. The area must also be covered by DEPARE or UNSARE objects as appropriate.

If it is required to encode one or more least depths in such an area, it must be done using a point object for each of the depths, in addition to the area object.

### 6.3.3 Danger line bordering an area through which navigation is not safe (see M4 -§420.1)

A danger line, bordering an area through which navigation is not safe, should be encoded using an OBSTRN object of type area, with attribute CATOBS = 6 (foul area).

## 6.4 Overfalls, races, breakers, eddies (see M4 - §423)

If it is required to encode a disturbance of water, it must be done using the object class WATTUR.

Geo object:	Water turbulence (WATTUR)
Attributes:	CATWAT	OBJNAM	NOBJNM	INFORM	NINFOM

Remarks:
- If it is required to encode a breaker over an off-lying shoal, it must be done using a WATTUR object at the same position as the feature causing the breaker.
- A WATTUR object of type area must be covered by DEPARE or UNSARE objects as appropriate.

## 6.5 Doubtful dangers (see M4 - §424)

The fact that a danger is doubtful should be encoded using the feature attributes QUASOU and STATUS and the spatial attribute QUAPOS on the object:

	M4	INT 1	QUAPOS	QUASOU	STATUS
Position approximate	424.1	IB7	4
Position doubtful	424.2	IB8	5
Existence doubtful	424.3	II1			18
Doubtful sounding	424.4	II2		3
Reported danger	424.5	II3	7 or 8	8 or 9
					table 6.4

Remarks:
- The same notions of approximate or doubtful positions and doubtful existence also apply to features other than dangers (e.g. landmarks, buoys).
- The text "Discoloured water" on the source indicates the probable existence of shallow water. This should be encoded using a CTNARE object with attribute INFORM or TXTDSC containing a cautionary note (see clause 6.6).

## 6.6 Caution areas

If it is required to identify an area in which the mariner must be aware of circumstances influencing the safety of navigation (e.g. an area of continually changing depths), it must be done using the object class CTNARE. This object class may be required to identify a danger, a risk, a rule or advice that is not directly related to a particular object.

Geo Object:	Caution area (CTNARE)
Attributes:	DATEND	DATSTA	PEREND	PERSTA	INFORM	NINFOM	TXTDSC
NTXTDS

# 7. Nature of the seabed

## 7.1 Description of the bottom (see M4 - §425)

If it is required to encode an area of the sea where the nature of the bottom is homogeneous, it must be done using the object class SBDARE.

Geo object:	Seabed area (SBDARE)

Figure 13 - Seabed areas
Attributes:	COLOUR	NATQUA	NATSUR
WATLEV	NOBJNM	OBJNAM
INFORM	NINFOM

Remarks:
In the following clauses, the paragraph prefixes refer to the examples shown in Figure 13.

(a)	Mixed natures: The dominant nature of the seabed should be given first. When there are qualifying terms associated with the various natures of surface, the qualifying terms must be listed in the same order as the nature of surface list. Where a particular nature of surface has no qualifying term, the place in the list must be left empty and a delimiting comma must be encoded. For example, to encode a bottom quality such as "fine sand, mud and broken shells", the attributes NATSUR = 4,1,17 and NATQUA = 1,,4 must be encoded as shown. Where the last nature of surface in a list has no qualifying term, a trailing comma must be encoded. For example, “fine sand and mud” must be encoded with NATSUR = 4,1 and NATQUA = 1,.

(b)	Underlying material: Should be encoded in the same way as mixed natures, replacing the comma by a slash (/). The surface layer must be given first, followed by the underlying layers.

(c)	Coral reef, which is always covered, represented as an area (IK16): An OBSTRN object of type area must be encoded with attributes CATOBS = 6 (foul area) and NATSUR = 14 (coral). This object must be covered by a DEPARE or UNSARE object as appropriate. In this area, some point dangers may be shown. An UWTROC object should be encoded for each individual point danger.

(d)	Hard bottom: The attribute NATQUA = 10 (hard) should be encoded, without being associated with NATSUR.

(e)	On the source, in the intertidal area or along the drying line, the nature of surface is sometimes shown by an open line rather than a closed area. In such cases, a SBDARE object of type line should be encoded, with attribute WATLEV = 4 (covers and uncovers).

(f)	If it is required to encode a rock pinnacle which is dangerous to navigation, it must be done using the object class UWTROC, while a rocky nature of seabed should be encoded using a SBDARE object of type point.

(g)	Where a SBDARE object of type area is located in an intertidal area, it should be encoded with WATLEV = 4 (covers and uncovers).
## 7.2 Special bottom types

### 7.2.1 Sand waves (see M4 - §428.1)

If it is required to encode sand waves, this must be done using the object class SNDWAV.

Geo object:	Sand waves (SNDWAV)
Attributes:	VERACC
VERLEN -	amplitude of the sand wave above the bottom
INFORM	NINFOM

### 7.2.2 Weed - Kelp (see M4 - §428.2)

If it is required to encode marine weed or kelp, it must be done using the object class WEDKLP.

Geo object:	Weed / kelp (WEDKLP)
Attributes:	CATWED	NOBJNM	OBJNAM	INFORM	NINFOM

### 7.2.3 Springs in the seabed (see M4 - §428.3)

If it is required to encode a spring from the seabed, it must be done using the object class SPRING.

Geo object:	Spring (SPRING)
Attributes:	NOBJNM	OBJNAM	INFORM	NINFOM

### 7.2.4 Tideways

If it is required to encode a tideway, it must be done using the object class TIDEWY.

Geo object:	Tideway (TIDEWY)
Attributes:	NOBJNM	OBJNAM	INFORM	NINFOM

Remarks:
TIDEWY objects must be covered by DEPARE, DRGARE or UNSARE objects.

8.	Sea areas (see M4 - §550)

Undersea features and sea areas in general, including intertidal areas, may be identified by their names and may be delimited by the spatial objects used by other geo objects (e.g. depth contours, coastlines). If it is required to encode these areas, this must be done using the object class SEAARE.

Geo object:	Sea area (SEAARE)
Attributes:	CATSEA	NOBJNM	OBJNAM	INFORM	NINFOM

Remarks:
- This object class has a use similar to that of the object class LNDRGN (see clause 4.7.1), but for the sea.
- A SEAARE object of type area should be bounded, if possible, by existing lines used by other objects (e.g. DEPCNT, COALNE). If necessary, however, this area may be bounded by other lines created to close the area, or to describe a new area.
- For seas, oceans, gulfs and other types of sea area, where there is no specific value for the attribute CATSEA, the generic term 'Sea', 'Ocean', 'Gulf', etc may be included in the attributes OBJNAM and NOBJNM.
- SEAARE objects of type area may overlap.
- A SEAARE object of type area must be covered by objects from Group 1 (DEPARE, DRGARE, UNSARE etc).

# 9. Harbour regulations

## 9.1 Regulations within harbour limits

### 9.1.1 Administrative harbour areas (see M4 - §430.1)

If it is required to encode an administrative harbour area, it must be done using the object class HRBARE.

Geo object:	Harbour area (HRBARE)
Attributes:	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

Remarks:
A masked line may be used to suppress the symbolisation of the boundary, where such symbolisation is considered inappropriate.

### 9.1.2 Speed limits (see M4 - §430.2)

Speed is often limited inside harbours in order to prevent wakes. If it is required to encode this restriction, it must be done using a RESARE object (see clause 11.1) with the attribute CATREA = 24 (no wake area) or RESTRN = 13 (no wake). If it is required to encode cases where the speed limit is known, it must be done using RESTRN = 27 (speed restricted), with the speed limit and its unit of measurement encoded using the attribute INFORM (e.g. Speed limit is 5 knots).

If it is required to encode the buoys/beacons marking the RESARE object with speed limits, it must be done using BCNSPP or BOYSPP objects (see clauses 12.3.1, 12.4.1), with the attribute CATSPM = 24 (“reduced wake” mark) or 25 (speed limit mark). The speed limit and its unit of measurement should be encoded using the attribute INFORM (e.g. Speed limit is 6 knots).

## 9.2 Anchorages and prohibited/restricted anchorages; moorings

### 9.2.1 Anchorages (see M4 - §431.1 and 431.3)

If it is required to encode an anchorage area, it must be done using the object class ACHARE.

Geo object:	Anchorage area (ACHARE)
Attributes:	CATACH	DATEND	DATSTA	NOBJNM
OBJNAM -	name or number of the anchorage
PEREND	PERSTA	RESTRN	STATUS
INFORM -	additional information about the category of anchorage
NINFOM

Remarks:
- Individual recommended anchorages without defined limits should be encoded as ACHARE objects of type point, with attributes CATACH = 1 (unrestricted anchorage) and STATUS = 3 (recommended).
- Areas with numerous small craft moorings (see M4 - §431.7) may be encoded as ACHARE objects of type area, with CATACH = 8 (small craft mooring area). For the encoding of mooring buoys, see clause 9.2.4.
- If it is required to encode an anchorage which may be used for a period of not more than 24 hours, it must be done using CATACH = 9 (anchorage for periods up to 24 hours).
- If it is required to encode an anchorage with a specific, limited time period, it must be done using CATACH = 10 (anchorage for limited period of time). The specific limit of time should be encoded using the attribute INFORM (e.g. Anchorage limited to 12 hours).

### 9.2.2 Anchor berths (see M4 - §431.2)

If it is required to encode an anchor berth, it must be done using the object class ACHBRT.

Geo object:	Anchor berth (ACHBRT)
Attributes:	CATACH	DATEND	DATSTA	NOBJNM
OBJNAM -	name or number of the berth
PEREND	PERSTA
RADIUS -	radius of the swinging circle in metres
STATUS
INFORM -	additional information about the category of anchorage
NINFOM

Remarks:
If an anchor berth is defined by a centre point and a swinging circle, it should be of type point, with the radius of the swinging circle encoded using the attribute RADIUS.

### 9.2.3 Anchoring restricted (see M4 - §431.4)

If it is required to encode a restricted anchoring area, it must be done using a RESARE object, or using other objects with the attribute RESTRN (see clause 11.1), where RESTRN = 1 (anchoring prohibited), 2 (anchoring restricted) or 7 (entry prohibited). Additional information about the restriction should be encoded using the attribute INFORM or TXTDSC.

### 9.2.4 Mooring buoys (see M4 - §431.5)

If it is required to encode a mooring buoy, it must be done using a MORFAC object (see clause 4.6.7.1), with attribute CATMOR = 7 (mooring buoy).

### 9.2.5 Mooring trots (see M4 - §431.6)

Figure 14 – Mooring trot
A complete mooring trot is composed of ground tackle, mooring cables, buoys and mooring berths on junction cables. The following remarks refer to the annotations in Figure 14 above:

(a)	Ground tackle should be encoded using OBSTRN objects (see clause 6.2.2), with attribute CATOBS = 9 (ground tackle).
(b)	Mooring cables should be encoded using CBLSUB objects (see clause 11.5.1), with attribute CATCBL = 6 (mooring cable/chain).
(c)	Buoys should be encoded using MORFAC objects (see clause 4.6.7.1), with attribute CATMOR = 7 (mooring buoy).
(d)	Mooring berths should be encoded using BERTHS objects (see clause 4.6.2).
(e)	Junction cables should be encoded using MORFAC objects (see clause 4.6.7.1), with attribute CATMOR = 6 (chain/wire/cable).

All of these objects should be aggregated using the collection object C_AGGR (see clause 15).

### 9.2.6 Anchorage - relationships

To encode an anchorage, objects such as ACHARE, ACHBRT, MORFAC, RESARE, C_AGGR (mooring trots) and the anchorage’s navigational aids objects may be associated using a collection object C_ASSO (see clause 15).

# 10. Recommended tracks and routes

## 10.1 Leading, clearing and transit lines and recommended tracks (see M4 - §433)

If it is required to encode leading, clearing and transit lines and recommended tracks, it must be done using the object classes NAVLNE and RECTRC, and related point navigational aids object classes. This applies for visual and radio navigational aids.

Relationships should be defined between these objects (see clauses 10.1.2 and 15)

NB. In North America the word ‘range’ is used instead of ‘transit’ and ‘leading line’.

### 10.1.1 Navigation lines and recommended tracks

If it is required to encode a navigation line, it must be done using the object class NAVLNE.

Geo object:	Navigation line (NAVLNE)
Attributes:	CATNAV	DATEND	DATSTA
ORIENT -	value of the bearing from seaward
PEREND	PERSTA	STATUS
INFORM -	legend as shown on the source
NINFOM

If it is required to encode a recommended track, it must be done using the object class RECTRC.

Geo object:	Recommended track (RECTRC)
Attributes:	CATTRK	DATEND	DATSTA
DRVAL1 -	minimum depth along the track
DRVAL2	NOBJNM	OBJNAM	ORIENT	PEREND	PERSTA	QUASOU	SOUACC	STATUS	TECSOU	TRAFIC	VERDAT
INFORM -	maximum authorised draft (e.g. Maximum authorised draft = 14 metres)
NINFOM

Remarks:
- The value 3 (recommended) should not be used on the attribute STATUS in this case because, by definition, RECTRC is recommended.
- In the case of a two-way recommended track, the value of orientation encoded on the attribute ORIENT should be the value of the bearing from seaward. If it is not possible to define a seaward direction, the value that is less than 180 should be used.
- When the traffic flow is one way, the direction of digitising of an object of type line should be the same as the direction of the traffic flow.

The use of NAVLNE and RECTRC is defined in more detail in the following table, and in Figure 15 below:

Figure 15		NAVLNE	RECTRC	Navigational aids
1	Recommended track on a leading line	CATNAV = 3	CATTRK = 1	at least 2
2	Clearing line on marks in line	CATNAV = 1	none	at least 2
3	Transit line on marks in line	CATNAV = 2	none	at least 2
4	Recommended track on a bearing	CATNAV = 3	CATTRK = 1	1
5	Clearing line on a bearing	CATNAV = 1	none	1
6	Transit line on a bearing	CATNAV = 2	none	1
7	Recommended track not based on fixed marks	none	CATTRK = 2	none
				table 10.1

Figure 15 – Navigation lines and recommended tracks

Remarks:
Even if, on the source, navigational aids are merged into only one symbol, one geo object must be created for each navigational aid.

### 10.1.2 Range systems - relationship

To encode a range system, the objects NAVLNE, RECTRC and the navigational aids objects should be aggregated using a collection object C_AGGR (see clause 15).

This aggregation object may also be associated, using a collection object C_ASSO (see clause 15), with the dangers (e.g. OBSTRN, WRECKS, UWTROC objects) marked by the clearing or transit line.

Figure 16 – Range systems

### 10.1.3 Measured distances (see M4 - §458)

If the track to be followed is on a leading line or a bearing, it must be encoded in the way described in Table 10.1 and Figure 15 above (cases 1 or 4). If the track is not on a leading line or bearing, it must be encoded only as a NAVLNE object with the attribute CATNAV being set to “unknown”. In either case, if it is required to encode the measured distance, it must be done using the attribute INFORM (e.g. Measured distance = 1450 metres).

If it is required to encode the transit lines, they must be done using NAVLNE objects, with CATNAV = 2 (transit line).

If it is required to encode the beacons, they must be done using BCNSPP objects, with attribute CATSPM = 17 (measured distance mark).

Where the entire measured distance system exists within a single cell, each transit line with its beacons must be aggregated into a collection object C_AGGR (see clause 15). These two aggregation objects and the track to be followed must be aggregated into another C_AGGR object.

## 10.2 Routeing measures

### 10.2.1 Traffic separation schemes

If it is required to encode a traffic separation scheme, it must be done using DWRTCL, DWRTPT, ISTZNE, PRCARE, TSELNE, TSEZNE, TSSBND, TSSCRS, TSSLPT, TSSRON objects, and navigational aids objects.

The encoding of relationships between these objects is defined in clause 10.2.3.

#### 10.2.1.1 Traffic separation scheme lanes (see M4 - §435.1)

A complete traffic separation scheme lane consists of one or more areas within which the flow of traffic follows one defined direction. If it is required to encode these areas, this must be done using the object class TSSLPT.

Geo object:	Traffic separation scheme lane part (TSSLPT)
Attributes:	CATTSS	DATEND	DATSTA
ORIENT -	direction of the traffic flow
RESTRN	STATUS	INFORM	NINFOM

Remarks:
At junctions, other than crossings and roundabouts, a separate TSSLPT object must be encoded. For this object, the attribute ORIENT must be omitted, in order to avoid implying that one lane has priority over another (see INT1 IM22). Warning text may be encoded using the attribute INFORM or TXTDSC.

Figure 17 - Junction
#### 10.2.1.2 Traffic separation scheme boundaries (see M4 - §435.1)

The object class TSSBND must only be used to encode the outer limits of traffic lanes or traffic separation scheme roundabouts.

Geo object:	Traffic separation scheme boundary (TSSBND)
Attributes:	CATTSS	DATEND	DATSTA	STATUS	INFORM	NINFOM

#### 10.2.1.3 Traffic separation lines (see M4 - §435.1)

The object class TSELNE must only be used to encode the common boundary of two traffic lanes, or of one traffic lane and one inshore traffic zone.

Geo object:	Traffic separation line (TSELNE)
Attributes:	CATTSS	DATEND	DATSTA	STATUS	INFORM	NINFOM

#### 10.2.1.4 Traffic separation zones (see M4 - §435.1)

The object class TSEZNE must only be used to encode the separation areas between two traffic lanes, or of one traffic lane and one inshore traffic zone, or to encode the centre part of a roundabout.

Geo object:	Traffic separation zone (TSEZNE)
Attributes:	CATTSS	DATEND	DATSTA	STATUS	INFORM	NINFOM

#### 10.2.1.5 Traffic separation scheme crossings (see M4 - §435.1)

The object class TSSCRS must only be used to encode the area where at least four traffic lanes cross.

Geo object:	Traffic separation scheme crossing (TSSCRS)
Attributes:	CATTSS	DATEND	DATSTA	RESTRN	STATUS	INFORM	NINFOM

Remarks:
- Junctions other than crossings and roundabouts should be encoded using the object class TSSLPT (see clauses 10.2.1.1 and 10.2.1.6).
- A TSSCRS object must not overlap a TSEZNE object at its centre.

#### 10.2.1.6 Traffic separation scheme roundabouts (see M4 - §435.1)

The object class TSSRON must only be used to encode the area in which traffic moves in a counter-clockwise direction around a specified point or zone.

Geo object:	Traffic separation scheme roundabout (TSSRON)
Attributes:	CATTSS	DATEND	DATSTA	RESTRN	STATUS	INFORM	NINFOM

Remarks:
A TSSRON object must not overlap a TSEZNE object at its centre.

#### 10.2.1.7 Inshore traffic zones (see M4 - §435.1)

The object class ISTZNE must only be used to encode the designated area between the landward boundary of a traffic separation scheme and the adjacent coast.

Geo object:	Inshore traffic zone (ISTZNE)
Attributes:	CATTSS	DATEND	DATSTA	RESTRN	STATUS	INFORM	NINFOM
#### 10.2.1.8 Precautionary areas (see M4 - §435.2)

The object class PRCARE must only be used to encode an area, within defined limits, where ships must navigate with particular caution, and within which the direction of traffic flow may be recommended.

Geo object:	Precautionary areas (PRCARE)
Attributes:	DATEND	DATSTA	RESTRN	STATUS	INFORM	NINFOM	TXTDSC
NTXTDS
Remarks:
A PRCARE object may overlap other objects encoded for the traffic separation scheme (e.g. TSSRON, TSSLPT, TSSCRS).

### 10.2.2 Deep water routes (see M4 - §435.3)

#### 10.2.2.1 Deep water route parts

A complete deep water route (DW) consists of one or more areas within which the flow of traffic either follows one defined direction for one-way traffic, or follows one defined direction and its reciprocal for two-way traffic. If it is required to encode these areas, this must be done using the object class DWRTPT.

Geo object:	Deep water route part (DWRTPT)
Attributes:	DATEND	DATSTA
DRVAL1 -	minimum depth
DRVAL2	NOBJNM
OBJNAM -	should only be used if the individual object is not aggregated in a collection object
ORIENT -	direction of the traffic flow
QUASOU	RESTRN	SOUACC	STATUS	TECSOU	TRAFIC	VERDAT	INFORM	NINFOM

Remarks:
- The route must be covered by DEPARE objects.
- A deep water route part may overlap a TSSLPT object.
To encode a complete deep water route, the DWRTCL, DWRTPT objects, and the navigational aids objects (if they are stated in the regulation defining the DW), may be aggregated using the collection object C_AGGR (see clause 15). The attribute OBJNAM on the C_AGGR object is used to encode the name of the DW, and the attribute INFORM or TXTDSC should be used to encode textual information about the whole DW.

#### 10.2.2.2 Deep water route centrelines

If it is required to encode the centreline of a deep water route, the width of which is not explicitly defined, it must be done using the object class DWRTCL.

Geo object:	Deep water route centreline (DWRTCL)
Attributes:	CATTRK	DATEND	DATSTA
DRVAL1 -	minimum depth
DRVAL2	NOBJNM
OBJNAM -	should only be used if the individual object is not aggregated in a collection object
ORIENT	QUASOU	SOUACC	STATUS	TECSOU	TRAFIC	VERDAT	INFORM	NINFOM

Remarks:
When the traffic flow is one way (attribute TRAFIC = 3), the direction of digitising should be the same as the direction of traffic flow.
### 10.2.3 Traffic separation scheme systems

To encode a traffic separation scheme (TSS) system, the DWRTCL, DWRTPT, ISTZNE, PRCARE, TSELNE, TSEZNE, TSSBND, TSSCRS, TSSLPT, TSSRON objects, and the navigational aids objects (if they are stated in the regulation defining the TSS or DW), must be aggregated using the collection object C_AGGR (see clause 15). The attribute OBJNAM for the C_AGGR object is used to encode the name of the TSS, and the attribute INFORM or TXTDSC should be used to encode textual information about the whole TSS.

### 10.2.4 Recommended routes (see M4 - §435.4)

If it is required to encode the centreline of a recommended route, it must be done using the object class RCRTCL.

Geo object:	Recommended route centreline (RCRTCL)
Attributes:	CATTRK	DATEND	DATSTA
DRVAL1 -	minimum depth
DRVAL2	NOBJNM	OBJNAM	ORIENT	PEREND	PERSTA	QUASOU	SOUACC	STATUS	TECSOU	TRAFIC	VERDAT
INFORM	NINFOM

Remarks:
When the traffic flow is one way (attribute TRAFIC = 3), the direction of digitising should be the same as the direction of traffic flow.

### 10.2.5 Recommended direction of traffic flow (see M4 - §435.5)

The object class RCTLPT should be used to encode areas with a recommended direction of traffic flow:
- between two TSS (INT1 - IM26.1)
- in the entrance area of a TSS
- along the outside of a deep water route (INT1 - IM26.2)

Geo object:	Recommended traffic lane part (RCTLPT)
Attributes:	DATEND	DATSTA	ORIENT	STATUS	INFORM	NINFOM

Remarks:
When the area is not defined, a point object should be encoded.

### 10.2.6 Two-way routes (see M4 - §435.6)

A two-way route consists of one or more areas within which traffic flows in two directions along one bearing and its reciprocal. If it is required to encode these areas, this must be done using the object class TWRTPT. These route parts will generally be two-way, but some may be restricted to one-way traffic flow (INT1 - IM28.2).

Geo object:	Two-way route part (TWRTPT)
Attributes:	CATTRK	DATEND	DATSTA
DRVAL1 -	minimum depth
DRVAL2	ORIENT	QUASOU	SOUACC	STATUS	TECSOU	TRAFIC	VERDAT	INFORM	NINFOM

Figure 18 – One-way traffic flow in a two-way route
If it is required to encode a two-way route with one-way sections, separate TWRTPT objects must be encoded for the different parts, with attribute TRAFIC = 3 (one-way) or 4 (two-way). In one-way sections, the attribute ORIENT must indicate the true direction of traffic flow, not its reciprocal. In two-way sections, ORIENT may indicate either direction of traffic flow.

### 10.2.7 Areas to be avoided (see M4 - §435.7)

If it is required to encode an area to be avoided, it must be done using a RESARE object (see clause 11.1), with attribute RESTRN = 14 (area to be avoided). An area to be avoided around a navigational aid must also be encoded with attribute CATREA = 12 (navigational aid safety zone).

## 10.3 Ferries (see M4 - §438)

If it is required to encode a ferry route, it must be done using the object class FERYRT.

Geo object:	Ferry route (FERYRT)
Attributes:	CATFRY	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA
STATUS	INFORM	NINFOM

## 10.4 Fairways

If it is required to encode a fairway, it must be done using the object class FAIRWY.

Geo object:	Fairway (FAIRWY)
Attributes:	DATEND	DATSTA
DRVAL1 -	minimum depth in the fairway
NOBJNM	OBJNAM	ORIENT	QUASOU	RESTRN	SOUACC	STATUS
TRAFIC	VERDAT	INFORM	NINFOM

Remarks:
- A collection object C_AGGR or C_ASSO (see clause 15) should be created to relate a fairway with associated navigational aids, recommended tracks, dredged areas, and other regulated areas.
- Where beacons or buoys marking a fairway are offset from the actual fairway limits, this should be indicated using the attribute INFORM on the FAIRWY object.

# 11. Regulated areas

## 11.1 Restricted areas in general (see M4 - §439.2 to § 439.4)

If it is required to encode a restricted area, it must be done using the object class RESARE, or using other object classes having the attribute RESTRN (ACHARE, CBLARE, DMPGRD, DRGARE, DWRTPT, FAIRWY, ICNARE, ISTZNE, MARCUL, MIPARE, OSPARE, PIPARE, PRCARE, SPLARE, SUBTLN, TESARE, TSSCRS, TSSLPT, TSSRON).

Geo object:	Restricted area (RESARE)
Attributes:	CATREA -	describes the reason for the regulation
DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA
RESTRN -	describes the restrictions
STATUS
INFORM -	a short explanation about the regulation (e.g. caution note from paper chart). The attribute TXTDSC may be used instead of INFORM, or for longer explanations or notes
NINFOM

Remarks:
If it is required to encode an area for which the mariner must be made aware of circumstances influencing the safety of navigation, it must be done using the object class CTNARE (see clause 6.6). This object class may be used to identify a danger, a risk, a rule or advice (e.g. an area of continually changing depths) which is not directly related to a particular object.

## Maritime jurisdiction areas (see M4 ‑ §440)
### 11.2.1 National territories

Figure 19 – Maritime jurisdiction areas

If it is required to encode a national territory, it must be done using the object class ADMARE.

Geo object:	Administration area (ADMARE)
Attributes:	JRSDTN -	2 - national
NATION	NOBJNM	OBJNAM	INFORM	NINFOM

### 11.2.2 Custom zones

If it is required to encode a custom zone, it must be done using the object class CUSZNE.

Geo object:	Custom zone (CUSZNE)
Attributes:	NATION	INFORM	NINFOM

### 11.2.3 Free port areas

If it is required to encode a free port area, it must be done using the object class FRPARE.

Geo object:	Free port area (FRPARE)
Attributes:	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

### 11.2.4 Territorial seas

A territorial sea is delimited by:
- territorial sea baselines (drying lines),
- straight territorial sea baselines,
- international maritime boundaries,
- seaward limits of territorial seas.
If it is required to encode the straight territorial sea baseline, it must be done using the object class STSLNE.

Geo object:	Straight territorial sea baseline (STSLNE)
Attributes:	NATION	INFORM	NINFOM

If it is required to encode the territorial sea area, it must be done using the object class TESARE.

Geo object:	Territorial sea area (TESARE)
Attributes:	NATION	RESTRN	INFORM	NINFOM

### 11.2.5 Contiguous zones

If it is required to encode a contiguous zone, it must be done using the object class CONZNE.

Geo object:	Contiguous zone (CONZNE)
Attributes:	DATEND	DATSTA	NATION	STATUS	INFORM	NINFOM

### 11.2.6 Fishery zones

If it is required to encode a fishery zone, it must be done using the object class FSHZNE.

Geo object:	Fishery zone (FSHZNE)
Attributes:	NATION	NOBJNM	OBJNAM	STATUS
INFORM -	value and unit of measure of the associated limit (e.g. 6 M or 12 M).
NINFOM

### 11.2.7 Continental shelves

If it is required to encode a continental shelf, it must be done using the object class COSARE.

Geo object:	Continental shelf area (COSARE)
Attributes:	NATION	NOBJNM	OBJNAM	INFORM	NINFOM

### 11.2.8 Exclusive economic zones

If it is required to encode an exclusive economic zone, it must be done using the object class EXEZNE.

Geo object:	Exclusive economic zone (EXEZNE)
Attributes:	NATION	INFORM	NINFOM

## 11.3 Military practice areas; submarine transit lanes; minefields

### 11.3.1 Military practice areas (see M4 - §441)

If it is required to encode a military practice area, it must be done using the object class MIPARE.

Geo object:	Military practice area (MIPARE)
Attributes:	CATMPA	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA	RESTRN	STATUS	INFORM	NINFOM

### 11.3.2 Submarine transit lanes (see M4 - §441.5)

If it is required to encode a submarine transit lane, it must be done using the object class SUBTLN.

Geo object:	Submarine transit lane (SUBTLN)
Attributes:	NOBJNM	OBJNAM	INFORM	NINFOM	RESTRN

### 11.3.3 Minefields (see M4 - §441.8)

If it is required to encode a minefield, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 14 (minefield). Former mined areas should also be encoded with attribute STATUS = 4 (not in use).

## 11.4 Dumping grounds (see M4 - §442)

If it is required to encode a dumping ground, it must be done using the object class DMPGRD.

Geo object:	Dumping ground (DMPGRD)
Attributes:	CATDPG	NOBJNM	OBJNAM	RESTRN	STATUS	INFORM	NINFOM

## 11.5 Cables and cable areas

### 11.5.1 Submarine cables (see M4 - §443)

If it is required to encode a submarine cable, it must be done using the object class CBLSUB.

Geo object:	Cable, submarine (CBLSUB)
Attributes:	BURDEP -	if the buried depth varies along the cable, the cable must be encoded as several objects.
CATCBL -	1 - power line
4 - telephone
5 - telegraph
6 - mooring cable/chain
if encoded, the value of CATCBL must be one of the above
CONDTN-	1 - under construction (during laying)
5 - planned construction (planned laying)
if encoded, the value of CONDTN must be one of the above
DATEND	DATSTA	DRVAL1	DRVAL2	NOBJNM	OBJNAM
STATUS -	4 - not in use (disused)
VERDAT	INFORM	NINFOM

Remarks:
Where a cable is disused, it should be encoded with the attribute STATUS = 4 (not in use (disused)), and the attribute CATCBL should not be encoded.

### 11.5.2 Overhead cables (see M4 - §382)

If it is required to encode an overhead cable, it must be done using the object class CBLOHD.

Geo object:	Cable, overhead (CBLOHD)
Attributes:	CATCBL
CONDTN-	1 - under construction
5 - planned construction
if encoded, the value of CONDTN must be one of the above
CONRAD	CONVIS	DATEND	DATSTA	ICEFAC	NOBJNM	OBJNAM
STATUS
VERACC -	applies only to VERCLR and VERCSA
VERCLR	VERCSA
VERDAT -	applies only to VERCLR and VERCSA
INFORM	NINFOM

Remarks:
- If it is required to encode telepheric cables, this must be done using CONVYR objects (see clause 4.8.11), with attribute CATCON = 1 (aerial cableway (telepheric)).
- Where a cable has radar reflectors, they must be encoded as separate RADRFL objects (see clause 12.12). If the whole cable is radar conspicuous, or the compilation scale is too small to show individual reflectors, the CBLOHD should be encoded with attribute CONRAD = 1 (radar conspicuous).

### 11.5.3 Submarine cable areas (see M4 - §443.2)

If it is required to encode a submarine cable area, it must be done using the object class CBLARE.

Geo object:	Cable area (CBLARE)
Attributes:	CATCBL -	1 - power line
4 - telephone
5 - telegraph
If encoded, the value of CATCBL must be one of the above
DATEND	DATSTA	NOBJNM	OBJNAM	RESTRN
STATUS -	used only to encode the status of the area and not the status of the cables in the area.
INFORM	NINFOM

## 11.6 Pipelines and pipeline areas

### 11.6.1 Pipelines, submarine or on land (see M4 - §377 and §444)

If it is required to encode a submarine or land pipeline, it must be done using the object class PIPSOL.

Geo object:	Pipeline, submarine / on land (PIPSOL)
Attributes:	BURDEP -	if the buried depth varies along the pipeline, the pipeline must be encoded as several objects
CATPIP
CONDTN -	1 - under construction (during laying)
5 - planned construction (planned laying)
if encoded, the value of CONDTN must be one of the above
DATEND	DATSTA
DRVAL1 -	shallowest depth over the pipeline
DRVAL2 -	deepest depth over the pipeline
NOBJNM	OBJNAM	PRODCT
STATUS -	4 - not in use (disused)
INFORM	NINFOM	VERACC	VERDAT	VERLEN

Remarks:
Where a pipeline is disused, it should be encoded with the attribute STATUS = 4 (not in use (disused)), and the attributes CATPIP and PRODCT should not be encoded.

### 11.6.2 Diffusers, cribs

If it is required to encode diffusers and cribs, this must be done using OBSTRN objects (see clause 6.2.2), with attribute CATOBS = 3 (diffuser) or 4 (crib).

### 11.6.3 Overhead pipelines (see M4 - §383)

If it is required to encode an overhead pipeline passing over or nearby navigable waters, it must be done using the object class PIPOHD.

Geo object:	Pipeline overhead (PIPOHD)
Attributes:	CATPIP
CONDTN -	1 - under construction
5 - planned construction
if encoded, the value of CONDTN must be one of the above
CONRAD	CONVIS	DATEND	DATSTA	NOBJNM	OBJNAM	PRODCT	STATUS
VERACC -	applies only to VERCLR
VERCLR
VERDAT	-	applies only to VERCLR
INFORM	NINFOM

Where an overhead pipeline is disused, it should be encoded with the attribute STATUS = 4 (not in use (disused)), and the attributes CATPIP and PRODCT should not be encoded.

### 11.6.4 Pipeline areas (see M4 - §444.2)

If it is required to encode a pipeline area, it must be done using the object class PIPARE.

Geo object:	Pipeline area (PIPARE)
Attributes:	CATPIP	CONDTN	DATEND	DATSTA	NOBJNM	OBJNAM	PRODCT	RESTRN
STATUS -	used only to encode the status of the area and not the status of the pipelines in the area.
INFORM	NINFOM

## 11.7 Oil and Gas fields

### 11.7.1 Wellheads (see M4 - §445.1, §445.5 and §445.7)

If it is required to encode wellheads, this must be done using OBSTRN objects of type point (see clause 6.2.2), with attributes:

CATOBS -	2 - wellhead
HEIGHT
STATUS -	4 - not in use (disused)
VALSOU
VERLEN -	vertical length of the wellhead above the seabed
WATLEV-	2 - always dry (for wellheads that protrude at high water)
3 - always under water/submerged

### 11.7.2 Offshore platforms (see M4 - §445.2)

If it is required to encode a permanent offshore platform, it must be done using the object class OFSPLF.

Geo object:	Offshore platform (OFSPLF)
Attributes:	CATOFP	COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA
HEIGHT -	for fixed platforms, referred to the vertical datum (see clause 2.1.2)
NATCON	NOBJNM	OBJNAM	PRODCT	STATUS	VERACC	VERDAT
VERLEN -	for floating platforms, referred to the sea level
INFORM	NINFOM

Remarks:
- If it is required to encode sites of dismantled platforms, this must be done using OBSTRN objects (see clause 6.2.2), with attribute CATOBS = 7 (foul ground).
- Platforms may carry lights (see clause 12.8), fog signals (see clause 12.5) and helicopter platforms (see clause 4.8.12).

### 11.7.3 Offshore safety zones (see M4 - §445.2)

If it is required to encode an offshore safety zone, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 1 (offshore safety zone).

### 11.7.4 Offshore production areas (see M4 - §445.3)

If it is required to encode an offshore production area, it must be done using the object class OSPARE.

Geo object:	Offshore production area (OSPARE)
Attributes:	CATPRA	CONDTN	CONRAD	CONVIS	DATEND	DATSTA	HEIGHT
 INFORM	NINFOM	NOBJNM	OBJNAM	PRODCT	RESTRN	STATUS
VERACC	VERLEN

### 11.7.5 Offshore tanker loading systems (see M4 - §445.4)

If it is required to encode an offshore tanker loading system, it must be done using the object class BOYINB (see clause 12.4.1).

If it is required to encode an articulated tower, it must be done using an OFSPLF object (see clause 11.7.2), with attribute:

CATOFP -	4 - articulated loading platform (ALP)
5 - single anchor leg mooring (SALM)
8 - floating production, storage and off-loading vessel (FPSO)
    10 - navigation, communication and control buoy (NCCB) (which may include storage facilities)

### 11.7.6 Flare stacks (see M4 - §445.6)

If it is required to encode a flare stack, it must be done using a LNDMRK object (see clause 4.8.15), with attribute CATLMK = 6 (flare stack).

An offshore flare stack may share the same geometry as the platform on which it is installed.

## 11.8 Spoil grounds, dredging areas (see M4 - §446)

If it is required to encode a spoil ground, it must be done using a DMPGRD object (see clause 11.4), with attribute CATDPG = 5 (spoil ground).

If it is required to encode a dredging area, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 21 (dredging area).

## 11.9 Fishing equipment and aquaculture areas

### 11.9.1 Fishing facilities (see M4 - §447.1 to §447.3)

If it is required to encode a fishing facilityit must be done using the object class FSHFAC.

Geo object:	Fishing facility (FSHFAC)
Attributes:	CATFIF	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	VERACC
VERLEN -	height of the object above the seabed
INFORM	NINFOM

### 11.9.2 Marine farms (see M4 - § 447.4 and §447.6)

If it is required to encode a marine farm, it must be done using the object class MARCUL.

Geo object:	Marine farm / culture (MARCUL)
Attributes:	CATMFA	DATEND	DATSTA	EXPSOU	INFORM	NINFOM	NOBJNM	OBJNAM	PEREND	PERSTA	QUASOU	RESTRN	SOUACC	STATUS	VALSOU	VERDAT
VERLEN -	height of the object above the seabed
WATLEV

When it is required to encode the minimum depth of the object, the attributes EXPSOU and QUASOU and the mandatory attribute VALSOU must be used. When a MARCUL object covers an area of the seafloor at the compilation scale of the ENC, the value of the attribute VALSOU represents the minimum depth, if known, over any structure used to form or support the marine farm, or within the area of the marine farm itself. The mandatory attribute WATLEV must be used to encode the water level of the shallowest section of the area, if partly or completely under water.

### 11.9.3 Fish havens (see M4 - §447.5)

If it is required to encode a fish haven, it must be done using an OBSTRN object (see clause 6.2.2), with attribute CATOBS = 5 (fish haven).

### 11.9.4 Fishing grounds

If it is required to encode a fishing ground, it must be done using the object class FSHGRD.

Geo object:	Fishing ground (FSHGRD)
Attributes:	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM	NINFOM

## 11.10 Degaussing ranges (see M4 - §448)

If it is required to encode a degaussing range, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 8 (degaussing range).

## 11.11 Historic wrecks (see M4 §449.5)

If it is required to encode a restricted area around a historic wreck, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 10 (historic wreck area).

In addition, the wreck itself should be encoded as a WRECKS object (see clause 6.2.1).

## 11.12 Seaplane landing areas (see M4 §449.6)

If it is required to encode a seaplane landing area, it must be done using the object class SPLARE.

Geo object:	Seaplane landing area (SPLARE)
Attributes:	NOBJNM	OBJNAM	PEREND	PERSTA	RESTRN	STATUS	INFORM
NINFOM

Remarks:
If it is required to encode an anchorage for seaplanes, it must be done using an ACHARE object (see clause 9.2.1), with attribute CATACH = 6 (seaplane anchorage).

## 11.13 Various maritime areas

### 11.13.1 Ice areas (see M4 - §449.1)

If it is required to encode an ice area, it must be done using the object class ICEARE.

Geo object:	Ice area (ICEARE)
Attributes:	CATICE	CONVIS	ELEVAT	HEIGHT	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	VERACC	VERDAT	VERLEN
INFORM	NINFOM

### 11.13.2 Log ponds (see M4 - §449.2)

If it is required to encode a log pond, it must be done using the object class LOGPON.

Geo object:	Log pond (LOGPON)
Attributes:	NOBJNM	OBJNAM	STATUS	INFORM	NINFOM

### 11.13.3 Incineration areas (see M4 - §449.3)

If it is required to encode an incineration area, it must be done using the object class ICNARE.

Geo object:	Incineration area (ICNARE)
Attributes:	NOBJNM	OBJNAM	PEREND	PERSTA	RESTRN	STATUS	INFORM
NINFOM

### 11.13.4 Cargo transhipment areas (see M4 - §449.4)

If it is required to encode a cargo transhipment area, it must be done using the object class CTSARE.

Geo object:	Cargo transhipment area (CTSARE)
Attributes:	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS
INFORM	NINFOM

## 11.14 Nature reserves

If it is required to encode a marine nature reserve area, it must be done using a RESARE object (see clause 11.1), with attribute CATREA = 4 (nature reserve). A nature reserve that is shown on the source as a point symbol should be encoded using a CTNARE object of type point, with the attribute INFORM = Marine nature reserve.

# 12. Aids to navigation

## 12.1 Lighthouses, navigational marks - relationships

### 12.1.1 Geo objects forming parts of navigational aids

Aids to navigation are composed of fixed or floating structures carrying equipment objects.

The most common structure objects are: BCNCAR, BCNISD, BCNLAT, BCNSAW, BCNSPP, BOYCAR, BOYINB, BOYISD, BOYLAT, BOYSAW, BOYSPP, BRIDGE, BUISGL, DAYMAR, LITFLT, LITVES, LNDMRK, MORFAC, OFSPLF, PILPNT, SLCONS.

Equipment objects consist of: DAYMAR, FOGSIG, LIGHTS, RADSTA, RDOSTA, RETRFL, RTPBCN, SISTAT, SISTAW, TOPMAR.

Radar reflectors must not be encoded as separate objects when attached to navigational aids. If it is required to encode their existence, it must be done using the attribute CONRAD = 3 (radar conspicuous (has radar reflector)) on the structure object.

Rescue stations and coastguard stations are not related directly to navigation, and they must not, therefore, be part of the equipment objects of navigational aids. If it is required to encode a rescue or coastguard station at the same location as a navigational mark, it must be encoded as a separate object, and share the same spatial object as the navigational aid.

### 12.1.2 Relationships

A master to slave relationship must be created in order to relate the different objects comprising a navigational aid.

When the navigational aid contains a structure object (from the above list), this object must be the master object, and the equipment objects must be the slaves.

When the nature of the base structure is unknown or there is no structure object, one of the equipment objects must be chosen as the master object, giving priority to a LIGHTS object, if one exists.

Figure 20 – Navigational aids
If it is required to encode the name of the navigational aid, it must be done using the attribute OBJNAM (and possibly the attribute NOBJNM) on the master object. The name should not be repeated for the slave objects. If the name is painted on the structure, it must be encoded with the same spelling in OBJNAM if it is based on the Latin alphabet. If the name is not based on the Latin alphabet, it must be encoded on NOBJNM, and transliterated for encoding on OBJNAM.

All point objects comprising a navigational aid must point to the same point spatial object.

The navigational aid may be associated with the objects which it marks (e.g. RESARE or OBSTRN objects) using the collection object C_ASSO (see clause 15). Several navigational aids and several marked objects may be associated in the same relationship.

## 12.2 Buoyage systems and direction of buoyage (see M4 - §461)

The buoyage system of the data set and, where necessary, the direction of buoyage, must be encoded using the meta object M_NSYS:

Meta object:	Navigational system of marks (M_NSYS)
Attributes:	MARSYS	ORIENT	INFORM	NINFOM

All parts of the data set containing data must be covered by M_NSYS objects, with the attribute MARSYS indicating the buoyage system in operation. M_NSYS with a value encoded for MARSYS must not overlap.
In the following table the symbol ‘/’ indicates that this attribute is not relevant for that particular object class. The table contains the most common examples of coding; other coding combinations are possible. For encoding of buoys, substitute BOY for BCN in Object class.

Feature	INT 1	Object class			CATCAM	COLOUR		COLPAT		MARSYS
North cardinal beacon	IQ 130.3	BCNCAR			1	2,6		1		1 and 2 / (IALA A and B)
East cardinal beacon	IQ 130.3	BCNCAR			2	2,6,2		1		1 and 2 / (IALA A and B)
South cardinal beacon	IQ 130.3	BCNCAR			3	6,2		1		1 and 2 / (IALA A and B)
West cardinal beacon	IQ 130.3	BCNCAR			4	6,2,6		1		1 and 2 / (IALA A and B)
Isolated danger beacon	IQ 130.4	BCNISD			/	2,3,2		1		1 and 2 / (IALA A and B)
Port lateral beacon	IQ 130.1	BCNLAT			1	3		/		1 (IALA A)
Starboard lateral beacon	IQ 130.1	BCNLAT			2	4		/		1 (IALA A)
Preferred channel to starboard lateral beacon	IQ 130.1	BCNLAT			3	3,4,3		1		1 (IALA A)
Preferred channel to port lateral beacon	IQ130.1	BCNLAT			4	4,3,4		1		1 (IALA A)
Port lateral beacon	IQ130.1	BCNLAT			1	4		/		2 (IALA B)
Starboard lateral beacon	IQ130.1	BCNLAT			2	3		/		2 (IALA B)
Preferred channel to starboard lateral beacon	IQ130.1	BCNLAT			3	4,3,4		1		2 (IALA B)
Preferred channel to port lateral beacon	IQ130.1	BCNLAT			4	3,4,3		1		2 (IALA B)
Safe water beacon	IQ130.5	BCNSAW			/	3,1 or 1,3		2		1 and 2 / (IALA A and B)
Special purpose beacon	IQ130.6	BCNSPP			/	6		/		1 and 2 / (IALA A and B)
Feature	INT 1	Object class			TOPSHP	COLOUR		COLPAT		MARSYS
North cardinal topmark	IQ 130.3	TOPMAR			13	2		/		1 and 2 / (IALA A and B)
East cardinal topmark	IQ 130.3	TOPMAR			11	2		/		1 and 2 / (IALA A and B)
South cardinal topmark	IQ 130.3	TOPMAR			14	2		/		1 and 2 / (IALA A and B)
West cardinal topmark	IQ 130.3	TOPMAR			10	2		/		1 and 2 / (IALA A and B)
Isolated danger topmark	IQ130.4	TOPMAR			4	2		/		1 and 2 / (IALA A and B)
Port lateral topmark	IQ130.1	TOPMAR			5	3		/		1 (IALA A)
Starboard lateral topmark	IQ130.1	TOPMAR			1	4		/		1 (IALA A)
Feature	INT 1	Object class			TOPSHP	COLOUR		COLPAT		MARSYS
Port lateral topmark	IQ130.1	TOPMAR			5	4		/		2 (IALA B)
Starboard lateral topmark	IQ130.1	TOPMAR			1	3		/		2 (IALA B)
Safe water topmark	IQ130.1	TOPMAR			3	3		2		1 and 2 / (IALA A and B)
Special purpose topmark	IQ130.1	TOPMAR			7	6		/		1 and 2 / (IALA A and B)
											table 12.1

Within a data set, there may be some areas where the direction of buoyage is defined by local rules and must, therefore, be specified. These areas should be encoded as separate M_NSYS area objects, with the attribute ORIENT indicating the direction of buoyage (MARSYS must not be encoded). M_NSYS objects with a value encoded for ORIENT must not overlap, but in areas where local buoyage directions apply, M_NSYS with a value encoded for ORIENT may overlap M_NSYS with a value encoded for MARSYS (see Figure 21 below).

Individual buoys and beacons may not be part of the general buoyage system. This should be encoded using MARSYS on these buoy and beacon objects.

Figure 21 – Buoyage system and direction

## 12.3 Fixed structures (see M4 - §455)

### 12.3.1 Beacons

If it is required to encode a beacon, it must be done using the object classes BCNCAR, BCNISD, BCNLAT, BCNSAW or BCNSPP.

Geo objects:	Beacon, cardinal (BCNCAR)
Beacon, isolated danger (BCNISD)
Beacon, lateral (BCNLAT)
Beacon, safe water (BCNSAW)
Beacon, special purpose (BCNSPP)
Attributes:	BCNSHP
CATCAM -	only for BCNCAR
CATLAM -	only for BCNLAT
CATSPM -	only for BCNSPP
COLOUR	COLPAT	CONDTN	CONRAD	CONVIS	DATEND	DATSTA
ELEVAT	HEIGHT
MARSYS -	only if different to the value encoded on meta object M_NSYS
NATCON	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
- If it is required to encode the altitude of the ground level above the vertical datum at the position of a beacon, it must be done using the attribute ELEVAT, but only for beacons built on land.
- If it is required to encode the total altitude of a beacon, including any equipment objects (e.g. topmark, light), above the vertical datum, it must be done using the attribute HEIGHT.
- If it is required to encode the total vertical length of a beacon, including any equipment objects (e.g. topmark, light), above the seabed or ground, it must be done using the attribute VERLEN.
- If it is required to encode a cairn that bears the colour(s) specified by a navigational system of marks, it must be done using a beacon object.
- If it is required to encode a beacon that has more than one colour, the attributes COLOUR and COLPAT must be encoded, according to the rules laid out in clause 2.4.

In the following table, the symbol ‘/’ indicates that this attribute does not exist for that particular object class. A blank indicates that the encoder may choose a relevant value for the attribute. The table contains the most common examples of coding; other coding combinations are possible.

Feature	INT1	Object-class	BCNSHP	CATSPM	Other attributes
Minor not permanent mark	IQ90 BCN*** 1 / IQ91 BCNLAT 1 / / IQ92 BCNLAT 2 /
Cairn	IQ100	BCN***	6
Coloured or white mark	IQ101	DAYMAR	/		NATCON = 9
Coloured topmark with function of beacon	IQ102.1	DAYMAR	/		NATCON = 9
Painted board with function of leading beacon	IQ102.2	DAYMAR	/	16	NATCON = 9, TOPSHP = 6
Beacon tower	IQ110	BCN***	3
Lattice beacon	IQ111	BCN***	4
Leading beacon	IQ120	BCNSPP		16
Beacon marking a clearing line	IQ121	BCNSPP		41
Beacon marking measured distance	IQ122	BCNSPP		17
Cable landing beacon	IQ123	BCNSPP		6
Outfall landing beacon	IQ123	BCNSPP		8
Pipeline landing beacon	IQ123	BCNSPP		39
Refuge beacon	IQ124	BCNSPP		44
Firing practice area beacon	IQ125	BCNSPP		1
Notice board	IQ126	BCNSPP		18
Buoyant beacon	IP5	BCN***	7
					table 12.2

### 12.3.2 Lighthouses (see M4 - § 457.3)

If it is required to encode a lighthouse, it must be done using a LNDMRK object (see clause 4.8.15), with attributes CATLMK = 17 (tower) and FUNCTN = 33 (light support) for towers, or using a BUISGL object (see clause 4.8.15), with the attribute FUNCTN = 33, for any other shapes.

If it is required to encode the attributes ELEVAT, HEIGHT and VERLEN for a lighthouse, this must be done as described in clause 12.3.1.

### 12.3.3 Daymarks

If it is required to encode a daymark, it must be done using the object class DAYMAR.

Geo object:	Daymark (DAYMAR)
Attributes:	CATSPM	COLOUR	COLPAT	DATEND	DATSTA	ELEVAT	HEIGHT	NATCON	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS
TOPSHP	VERACC	VERDAT	VERLEN	INFORM	NINFOM

Remarks:
If it is required to encode the attributes ELEVAT, HEIGHT and VERLEN for a daymark, this must be done as described in clause 12.3.1.

## 12.4 Floating structures (see M4 - §460)

### 12.4.1 Buoys

If it is required to encode a buoy, it must be done using the object classes BOYCAR, BOYINB, BOYISD, BOYLAT, BOYSAW or BOYSPP.

Geo objects:	Buoy, cardinal (BOYCAR)
Buoy, installation (BOYINB)
Buoy, isolated danger (BOYISD)
Buoy, lateral (BOYLAT)
Buoy, safe water (BOYSAW)
Buoy, special purpose (BOYSPP)
Attributes:	BOYSHP
CATCAM -	only for BOYCAR
CATINB -	only for BOYINB
CATLAM -	only for BOYLAT
CATSPM -	only for BOYSPP
COLOUR	COLPAT	CONRAD	DATEND	DATSTA
MARSYS -	only if different to the value encoded on meta object M_NSYS
NATCON	NOBJNM	OBJNAM	PEREND	PERSTA
PRODCT -	only for BOYINB
STATUS	-	VERACC	VERLEN	INFORM	NINFOM

Remarks:
- If it is required to encode the total vertical length, including any equipment objects (e.g. topmark, light), of the buoy above the water level, it must be done using the attribute VERLEN.
- If it is required to encode a buoy that has more than one colour, the attributes COLOUR and COLPAT must be encoded, according to the rules laid out in clause 2.4.

In the following table, the symbol ‘/’ indicates that this attribute does not exist for that particular object class. A blank indicates that the encoder may choose a relevant value for the attribute. The table contains the most common examples of coding; other coding combinations are possible.

Feature	INT1	Object-class	BOYSHP	CATSPM	Other attributes
Mooring buoy	IQ40	MORFAC		/	CATMOR = 7
Oil or gas installation buoy	IL16	BOYINB	7	/	PRODCT = 1 or 2, CATINB = 1 or 2
Firing danger area buoy	IQ50	BOYSPP		1
Target	IQ51	BOYSPP		2
Marker ship	IQ52	BOYSPP		3
Barge	IQ53	BOYSPP		5
Degaussing range buoy	IQ54	BOYSPP		4
Buoy marking cable	IQ55	BOYSPP		6
Spoil ground buoy	IQ56	BOYSPP		7
Buoy marking outfall	IQ57	BOYSPP		8
Buoy marking pipeline		BOYSPP		39
Superbuoy	IQ26	BOY***	7
Large automatic navigational buoy	IP6	BOYSPP	7	15
Data-collecting buoy of superbuoy size	IQ58	BOYSPP	7	9
Buoy marking wave recorder (or current meter)	IQ59	BOYSPP		10	INFORM = wave recorder (e.g.)
Seaplane anchorage buoy	IQ60	BOYSPP		11
Buoy marking traffic separation scheme	IQ61	BOYSPP		19
Buoy marking recreation zone	IQ62	BOYSPP		12
					table 12.3

### 12.4.2 Light floats and light vessels (see M4 - § 462.8 and §474.1)

If it is required to encode a light float or a light vessel, it must be done using the object class LITFLT or LITVES.

Geo objects:	Light float (LITFLT)
Light vessel (LITVES)
Attributes:	COLOUR	COLPAT	CONRAD	CONVIS	DATEND	DATSTA	HORACC	HORLEN	HORWID	NATCON	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	VERACC	VERLEN	INFORM	NINFOM

## 12.5 Fog signals (see M4 - §451)

If it is required to encode a fog signal, it must be done using the object class FOGSIG.

Geo object:	Fog signal (FOGSIG)
Attributes:	CATFOG	DATEND	DATSTA	NOBJNM	OBJNAM	SIGFRQ	SIGGEN
SIGGRP	SIGPER	SIGSEQ	STATUS	VALMXR	INFORM	NINFOM

## 12.6 Topmarks (see M4 - §463)

If it is required to encode a topmark, it must be done using the object class TOPMAR.

Geo object:	Topmark (TOPMAR)
Attributes:	COLOUR	COLPAT
HEIGHT
MARSYS	-	the value is given on meta object M_NSYS or MARSYS for the structure object
STATUS	TOPSHP	VERACC	VERDAT	VERLEN	INFORM	NINFOM

## 12.7 Retro-reflectors

If it is required to encode a retro-reflector, it must be done using the object class RETRFL.

Geo object:	Retro-reflector (RETRFL)
Attributes:	COLOUR	COLPAT	HEIGHT
MARSYS	-	the value is given on meta object M_NSYS or MARSYS for the structure object
STATUS	VERACC	VERDAT
INFORM -	describes letters, patterns or numerals shown on the retro-reflector
NINFOM

## 12.8 Lights (see M4 - §470)

If the actual structure that supports a light in a water area is unknown, a PILPNT object with no attributes should also be encoded at the same position as the light.

12.8.1	Description of lights

If it is required to encode a light and its sectors, each sector of the light must be encoded using one separate LIGHTS object. These objects must be slave objects of the same master object, which is either the structure object or one of the LIGHTS, so that the relationship between them is indicated using the master/slave relationship mechanism described in clause 12.1.2.

Geo object:	Light (LIGHTS)
Attributes:	CATLIT -	mandatory for air obstruction and fog detector lights
COLOUR -	mandatory except for air obstruction and fog detector lights
DATEND	DATSTA	EXCLIT
HEIGHT -	prohibited for floating lights
LITCHR -	mandatory except for air obstruction and fog detector lights
LITVIS	MARSYS	MLTYLT	NOBJNM	OBJNAM
ORIENT -	prohibited, except for directional or moiré effect lights
PEREND	PERSTA
SECTR1 -	only for sector lights
SECTR2 -	only for sector lights
SIGGRP -	prohibited for fixed lights
SIGPER -	prohibited for fixed lights
SIGSEQ -	prohibited for fixed lights
STATUS	VALNMR	VERACC
VERDAT -	applies only to HEIGHT; this value must only be encoded if it is different to the value encoded in the VDAT subfield of the Data Set Parameter (DSPM) field, or different to the value of VERDAT encoded on meta object M_VDAT
INFORM	NINFOM

Remarks:
- If it is required to encode details of the lighting technology (e.g. neon), it must be done using the attribute INFORM.
- If it is required to encode the purpose of a marine spotlight, it must be done using INFORM.

### 12.8.2 Types and functions of lights (see M4 - §471.1)

If it is required to encode types and functions of lights, this must be done using the attribute CATLIT.

### 12.8.3 Rhythms of lights (see M4 - §471.2)

If it is required to encode the rhythms of lights, this must be done using the attributes LITCHR and SIGGRP.

The use of these attributes is defined in the following table; it contains the most common examples of coding; other coding combinations are possible:

Rhythms of lights	F	Oc	Oc(2)	Oc(2+3)	Iso	Fl	Fl(3)	LFl
LITCHR	1	8	8	8	7	2	2	3
SIGGRP	prohibited	(1)	(2)	(2+3)	(1)	(1)	(3)	(1)

Rhythms of lights	Q	Q(3)	IQ	VQ	VQ(3)	IVQ	UQ	IUQ
LITCHR	4	4	9	5	5	10	6	11
SIGGRP	(1)	(3)	( )	(1)	(3)	( )	(1)	( )

Rhythms of lights	Mo(K)	FFl	Q(6)+LFl	VQ(6)+LFl	Al.WR	Al.Fl.WR	Al.Fl(2W+1R)	Al.Oc(4)WR
LITCHR	12	13	25	26	28	19	19	17
SIGGRP	(K)	()(1)	(6)(1)	(6)(1)	( )	(1)	(2+1)	(4)
table 12.4

Some lights recently constructed may appear to the mariner as "fixed and flashing - FFL" by night, while the real world object actually comprises two separate lights vertically disposed, one fixed and the other flashing (F&Fl). When it is known that two separate features actually exist, they must be encoded as separate objects, in this case two LIGHTS objects, one with attribute LITCHR = 1 (fixed) and the other with LITCHR = 2 (flashing), and not as one LIGHTS with LITCHR = 13 (fixed and flashing).

### 12.8.4 Elevations of lights (see M4 - §471.6)

If it is required to encode the elevation of a light on a fixed structure, it must be done using the attribute HEIGHT.

If it is required to encode the height above the water surface of a light on a floating structure, it must be done using the attribute INFORM on the LIGHTS object.

### 12.8.5 Times of exhibition and exhibition conditions

### 12.8.5.1 Night lights

If it is required to encode a night light, it must be done using a LIGHTS object, with attribute EXCLIT = 4 (night light).

### 12.8.5.2 Unwatched lights (see M4 - §473.1)

This information should not be encoded, but unwatched (unmanned) lights, with no standby or emergency arrangements, may be encoded using attribute STATUS = 17 (unwatched).

### 12.8.5.3 Occasional lights (see M4 - §473.2)

If it is required to encode an occasional light, it must be done using attribute STATUS = 2 (occasional). If it is required to encode a private light that is not regularly exhibited, it must be done using STATUS = 2,8 (occasional, private).

### 12.8.5.4 Daytime lights (see M4 - §473.4)

If it is required to encode a daytime light, it must be done using attribute EXCLIT = 1 (light shown without change of character).

If it is required to encode a light having characteristics shown by day different to those shown at night, it must be done by encoding two LIGHTS objects sharing the same point spatial object:
- one LIGHTS object with EXCLIT = 2 (daytime light),
- one LIGHTS object with EXCLIT = 4 (night light).

### 12.8.5.5 Fog lights (see M4 - §473.5)

If it is required to encode a fog light , it must be done using a LIGHTS object, with attributes EXCLIT = 3 (fog light) and STATUS = 2 (occasional).

If it is required to encode a light having characteristics shown in fog that are different to those shown in conditions of normal visibility, it must be done by encoding two LIGHTS objects sharing the same point spatial object:
- one LIGHTS object with EXCLIT = 3 (fog light) and STATUS = 2 (occasional)
- one LIGHTS object with EXCLIT = 2 (daytime light) or 4 (night light) and attribute INFORM = Character of the light changes in fog.

### 12.8.6 Sector lights and lights not visible all round (see M4 - §475)

### 12.8.6.1 Sector lights (see M4 - §475.1)

Each sector in which the light is visible from seaward must be encoded as one LIGHTS object.

There must be no object created to encode a sector where no light is exhibited.

Limits of sectors must be encoded using attributes SECTR1 and SECTR2.
#### 12.8.6.2 Lights obscured by obstructions (see M4 - §475.3)

Figure 22 – Obscured light sectors

If an encoded light is obscured in a part of the navigable area of a sector (see Figure 22 - A) beyond an offshore obstruction, it must be encoded as several LIGHTS objects. The partially obscured sector of (b), seaward of the island, must be encoded as a LIGHTS object, with attributes LITVIS = 8 (partially obscured) and INFORM = Sector obscured only beyond .…. The sectors in which the light is visible from seaward ((a) and (c)) must be encoded as separate LIGHTS objects.

If there is no navigable water between the light and the obstacle (see Figure 22 - B), the masked sector must be encoded as a LIGHTS object, with LITVIS = 3 (faint) or 7 (obscured).

#### 12.8.6.3 White fairway sectors (see M4 - §475.5)

The light sectors must be encoded as separate LIGHTS objects. The fairway defined by the succession of navigable areas in the white sectors may be encoded using the object class FAIRWY (see clause 10.4).

#### 12.8.6.4 Leading lights (see M4 - §475.6)

If it is required to encode a leading light, it must be done using a LIGHTS object, with attribute:

 CATLIT =	4,12 - front leading light
4,13 - rear leading light
4,14 - lower leading light
4,15 - upper leading light

Remarks:
- The attribute ORIENT must not be used for leading lights, except for directional lights.
- Even if, on the source, the leading lights are merged into a single symbol, at least one LIGHTS object must be created for each light.
- The leading line must be encoded using the method described in clause 10.1.
#### 12.8.6.5 Directional lights (see M4 - §475.7)

If it is required to encode a directional light, it must be done using a LIGHTS object, with attribute CATLIT = 1 (directional function) and, if the light is intensified in this sector, with attribute LITVIS = 4 (intensified).

The attribute ORIENT must be encoded to indicate the orientation, measured from seaward, of the leading line of the directional light.

If it is required to encode the recommended track, it must be done using the method described in clause 10.1.

#### 12.8.6.6 Moiré effect lights (see M4 - §475.8)

If it is required to encode a moiré effect light, it must be done using a LIGHTS object, with attribute CATLIT = 16 (moire effect).

The attribute ORIENT must be encoded to indicate the orientation, measured from seaward, of the leading line of the moiré effect light.

If it is required to encode the recommended track, it must be done using the method described in clause 10.1.

### 12.8.7 Various special types of lights

Type	M-4	CATLIT	Remarks
Subsidiary light	471.8	10
Aero light	476.1	5
Air obstruction light	476.2	6
Fog detector light	477	7
Bearing light	478.1	18
Flood light	478.2	8	Only to encode flood lights that are visible from seaward. The illuminated structure should be encoded using appropriate object classes, with attribute STATUS = 12 (illuminated)
Synchronised lights	478.3		STATUS =15. Synchronised lights may be associated using the collection object C_ASSO
Strip light	478.5	9
Spot light		11	Only to encode spot lights that are visible from seaward. The illuminated feature should be encoded using appropriate object classes, with attribute STATUS = 12 (illuminated)
Emergency light		17	Must be encoded as a separate object to the main LIGHTS object
Horizontally disposed lights	471.8	19	The number of lights must be encoded using attribute MLTYLT
Vertically disposed lights	471.8	20	The number of lights must be encoded using attribute MLTYLT
			table 12.5

### 12.8.8 Light structures

If a light that is on a fixed structure is located in a water area and the structure that supports it is unknown, a PILPNT object with no attributes should also be encoded at the same position as the light. This will ensure that a symbol will be shown on ECDIS systems when the LIGHTS objects are not displayed during daytime navigation.

## 12.9 Radio stations (see M4 - §480 to §485)

If it is required to encode a radio station, it must be done using the object class RDOSTA.

Geo object:	Radio station (RDOSTA)
Attributes:	CALSGN	CATROS	COMCHA	DATEND	DATSTA	ESTRNG	NOBJNM
OBJNAM	ORIENT	PEREND	PERSTA	SIGFRQ	STATUS	INFORM
NINFOM

Remarks:
- The RDOSTA must only be used to encode the technical equipment itself, independent of the building or structure in which it is installed. If it is required to encode the building or structure (e.g. mast, tower, radar dome), it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).
- Further information (e.g. transmission characteristic) may be encoded using attribute INFORM or TXTDSC.

### 12.9.1 Marine and aero-marine radiobeacons (see M4 - §481)

If it is required to encode a marine and aero-marine radiobeacon, it must be done using a RDOSTA object, with attributes:

CATROS -	1 - circular (omni-directional) marine or aero-marine radiobeacon
2 - directional radiobeacon
3 - rotating-pattern radiobeacon
4 - Consol beacon
ORIENT -	value of the bearing from seaward. Applies only for CATROS = 2.

Remarks:
If it is required to encode the bearing line and the recommended track for a directional radiobeacon, it must be done as described in clause 10.1. Where the bearing line coincides with a leading line defined by lights or other visual features making up a range system, navigation lines and recommended tracks must not be duplicated. The objects making up the range system must be aggregated using the collection object C_AGGR (see clause 10.1.2).

### 12.9.2 Aeronautical radiobeacons (see M4 - §482)

If it is required to encode an aeronautical radio beacon, it must be done using a RDOSTA object, with attribute CATROS = 7 (aeronautical radiobeacon). The identification signal may be encoded using the attribute CALSGN.

### 12.9.3 Radio direction-finding stations (see M4 - §483)

If it is required to encode a radio direction-finding station, it must be done using a RDOSTA object, with attribute CATROS = 5 (radio direction-finding station). The identification signal may be encoded using the attribute CALSGN.

### 12.9.4 Coast radio stations providing QTG service (see M4 - §484)

If it is required to encode a coast radio station which provides a QTG service, it must be done using a RDOSTA object, with attribute CATROS = 6 (coast radio station providing QTG service).

## 12.10 Radar beacons (see M4 - §486)

If it is required to encode a radar beacon, it must be done using the object class RTPBCN.

Geo object:	Radar transponder beacon (RTPBCN)
Attributes:	CATRTB	DATEND	DATSTA	NOBJNM	OBJNAM	RADWAL	SECTR1	SECTR2
SIGGRP -	morse identification letter(s)
SIGSEQ	STATUS	VALMXR	INFORM	NINFOM

Remarks:
- The RTPBCN must only be used to encode the technical equipment itself, independent of the building or structure in which it is installed. If it is required to encode the building or structure (e.g. mast, tower, radar dome), it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).
- If it is required to encode the bearing line and the recommended track for leading racons, it must be done as described in clause 10.1. Where the bearing line coincides with a leading line defined by lights or other visual features making up a range system, navigation lines and recommended tracks must not be duplicated. The objects making up the range system must be aggregated using the collection object C_AGGR (see clause 10.1.2).
- The sweep period may be encoded using the attribute INFORM.

## 12.11 Radar surveillance systems (see M4 - §487)

If it is required to encode a radar surveillance system, it must be done using the object classes RADRNG, RADLNE and RADSTA.

### 12.11.1 Radar ranges (see M4 - §487.1)

If it is required to encode a radar range, it must be done using the object class RADRNG.

Geo object:	Radar range (RADRNG)
Attributes:	COMCHA	DATEND	DATSTA	NOBJNM	OBJNAM	STATUS	INFORM
NINFOM

Remarks:
RADRNG objects must be of type area.

### 12.11.2 Radar reference lines (see M4 - §487.2)

If it is required to encode a radar reference line, it must be done using the object class RADLNE.

Geo object:	Radar line (RADLNE)
Attributes:	NOBJNM	OBJNAM
ORIENT -	value of the bearing from seaward
STATUS	INFORM	NINFOM

### 12.11.3 Radar station (see M4 - §487.3)

If it is required to encode a radar station, it must be done using the object class RADSTA.

Geo object:	Radar station (RADSTA)
Attributes:	CATRAS	COMCHA	DATEND	DATSTA
HEIGHT -	height of the emitting part of the radar
NOBJNM	OBJNAM	STATUS	VERACC	VALMXR	VERDAT	INFORM	NINFOM

Remarks:
The RADSTA must only be used to encode the technical equipment itself, independent of the building or structure in which it is installed. If it is required to encode the building or structure (e.g. mast, tower, radar dome) it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).

## 12.12 Radar conspicuous objects (see M4 - §485.2)

The attribute CONRAD (conspicuous, radar) is used to encode whether or not an object is radar conspicuous.

Remarks:
- If it is required to encode an object which has no radar reflector, but is radar conspicuous, it must be indicated using attribute CONRAD = 1 (radar conspicuous) on the object.
- If it is required to encode an area or point object which is radar conspicuous because it is fitted with a radar reflector, it must be indicated using CONRAD = 3 (radar conspicuous (has radar reflector)) on the object.
- If it is required to encode radar reflectors on line objects (e.g. overhead cables), this must be done using the object class RADRFL.

Geo object:	Radar reflector (RADRFL)
Attributes:	HEIGHT	STATUS	VERACC	VERDAT	INFORM	NINFOM
## 12.13 Radio reporting (calling-in) points (see M4 - §488)

If it is required to encode a radio reporting point or line, it must be done using the object class RDOCAL.

Geo object:	Radio calling-in point (RDOCAL)
Attributes:	COMCHA	DATEND	DATSTA	NOBJNM
OBJNAM -	e.g. alphanumeric designator
ORIENT -	orientation of the traffic flow at that point
PEREND	PERSTA	STATUS	TRAFIC
INFORM -	notes; for example, if the requirement to report by radio relates to certain classes of vessels only. The attribute TXTDSC may be used instead of INFORM, or for longer explanations or notes
NINFOM

Remarks:
- Each RDOCAL object must only carry one orientation. If it is required to encode the reciprocal orientation, to indicate that a bearing and its opposite apply to a RDOCAL object, it must be done using attribute TRAFIC = 4 (two-way). If the same position is used for another orientation (not opposite) of traffic flow, an additional RDOCAL object must be created.
- RDOCAL objects of type line should be digitised such that the traffic direction that is required to report is to the right.

# 13. Marine services and signal stations

## 13.1 Pilot stations (see M4 - §491)

### 13.1.1 Pilot stations ashore (see M4 - §491.3 and 491.4)

If it is required to encode a pilot station, it must be done using a BUISGL or LNDMRK object, with attribute FUNCTN = 11 (pilot office) or 12 (pilot lookout).

### 13.1.2 Pilot boarding places (see M4 - §491.2)

If it is required to encode a pilot boarding place, it must be done using the object class PILBOP.

Geo object:	Pilot boarding place (PILBOP)
Attributes:	CATPIL	COMCHA	DATEND	DATSTA	NOBJNM	NPLDST	OBJNAM	PEREND	PERSTA	PILDST	STATUS	INFORM	NINFOM

## 13.2 Coastguard stations (see M4 - §492)

If it is required to encode a coastguard station, it must be done using the object class CGUSTA.

Geo object:	Coastguard station (CGUSTA)
Attributes:	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS
INFORM	NINFOM

Remarks:
The CGUSTA must only be used to describe the function of the coastguard station, independent of the building or structure itself. If it is required to encode the building or structure in which the coastguard station operates, it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).

## 13.3 Rescue stations (see M4 - §493)

If it is required to encode a rescue station, it must be done using the object class RSCSTA.

Geo object:	Rescue station (RSCSTA)
Attributes:	CATRSC	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM	NINFOM

Remarks

- The RSCSTA must only be used to describe the function of the rescue station, independent of the building or structure itself. If it is required to encode the building or structure housing the service, it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).
- If it is required to encode a refuge beacon, it must be done using a BCNSPP object, with attribute CATSPM = 44 (refuge beacon), not by using RSCSTA.
## 13.4 Signal stations (see M4 - §494 to §497)

If it is required to encode a signal station, it must be done using traffic signal stations or warning signal stations.

Geo object:	Signal station, traffic (SISTAT)
Attributes:	CATSIT	COMCHA	DATEND	DATSTA	NOBJNM	OBJNAM	PEREND	PERSTA	STATUS	INFORM	NINFOM

Remarks:
If it is required to encode a bridge light marking the centre of a navigable span, it must be done using the object class LIGHTS.
The SISTAT must only be used to describe the function of the signal station, independent of the building or structure itself. If it is required to encode the building or structure housing the service, it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).

Geo object:	Signal station, warning (SISTAW)
Attributes:	CATSIW	COMCHA	DATEND	DATSTA	NOBJNM	OBJNAM
PEREND	PERSTA	STATUS	INFORM	NINFOM

Remarks:
The SISTAW must only be used to describe the function of the signal station, independent of the building or structure itself. If it is required to encode the building or structure housing the service, it must be done using an appropriate object class (e.g. BUISGL, LNDMRK).

# 14. Geographic names

If it is required to encode an international or national geographic name, it must be done using attributes OBJNAM and NOBJNM as described in the ENC Product Specification (S-57 Appendix B.1), clause 3.11. The use of the cartographic object $TEXTS is prohibited.

When possible, existing objects (e.g. BUAARE, RIVERS, navigational marks) should be used to carry this information.

If it is required to encode a geographic name for which there is no existing object, a specific ADMARE, SEAARE or LNDRGN object must be created (see clauses 4.7.1 and 8). In order to minimise the data volume, these objects should, where possible, use the geometry of existing objects, e.g. a SEAARE object may use the geometry of a DEPARE object.

Geographic names should be encoded using OBJNAM based on the following criteria and at the producing authority’s discretion:

Named points or capes that do not contain navigational aids should be encoded as LNDRGN objects (of type area or point), with the geographic name encoded using OBJNAM.

Named points or capes that contain one navigational aid should be encoded using OBJNAM on the master object associated with the navigational aid. If more than one navigational aid exists on the point or cape, a LNDRGN object (of type area or point) should be encoded, with the geographic name encoded using OBJNAM .

A group of hydrographic objects (e.g. SBDARE, UWTROC, OBSTRN), associated with a particular geographic name, should have the name encoded using OBJNAM on a SEAARE object (of type area or point). The name should not be encoded on the individual hydrographic objects.

A major island name close to primary shipping corridors should be encoded using OBJNAM on the LNDARE object delimiting the island. A group of islands associated with a geographic name should have the name encoded using OBJNAM on a LNDRGN object (of type area or point), or a collection object C_ASSO.

Named features listed in HOs’ Sailing Directions that may assist in navigation should be encoded using OBJNAM on the relevant object (e.g. LNDRGN, UWTROC, SBDARE, SEAARE, OBSTRN).

If it is required to encode an administrative area of international, national, provincial or municipal jurisdiction that may have legal inference, it must be done using an ADMARE object, with the name encoded using OBJNAM.

If it is required to encode a major city along the coast, it must be done using BUAARE or ADMARE objects (see clause 4.8.14), with the name encoded using OBJNAM.

If it is required to encode the name of a navigable river, lake or canal, it must be done using a SEAARE object, with the name encoded using OBJNAM.

In all instances, if the exact extent of the feature to be named is known, an area object must be created. If the exact extent is not known, an existing or specifically encoded point object should be used to encode the geographic name.

# 15. Collection objects

If it is required to identify an aggregation or association between two or more objects, it must be done using the object classes C_AGGR or C_ASSO.

Collection object:	Aggregation (C_AGGR)
Attributes:	NOBJNM	OBJNAM	INFORM	NINFOM

C_AGGR objects should be used to encode the link between objects that are functionally related and which together form a higher level entity. For example, a navigation line, a recommended track and the defining navigational aids should be linked using a C_AGGR object to form a range system.

Collection object:	Association (C_ASSO)
Attributes:	NOBJNM	OBJNAM	INFORM	NINFOM

C_ASSO objects should be used to encode the association between two or more objects. The association does not create any higher level entity. For example, a wreck should be associated with the buoy that marks it.

The following table shows the most common examples of the application of collection objects. Other applications for collection objects are possible.

Relationships	FFPT field	collection object	comment
Mooring trots	peer *	C_AGGR	see 9.2.5
Measured distances	peer *	C_AGGR	see 10.1.3
Traffic Separation Schemes systems	peer *	C_AGGR	see 10.2.3
Navigation lines and tracks	peer *	C_AGGR	see 10.1.2
Navigation lines, tracks and dangers	peer *	C_ASSO	see 10.1.2 **
Synchronised lights	peer *	C_ASSO	see 12.8.7
Airfield, airport, (runway, control etc.)	peer *	C_ASSO	see 4.8.12
Tide, tidal stream (non-harmonic prediction – time series or harmonic prediction)	peer *	C_ASSO	see 3.2.3, 3.3.3 and 3.3.4
Anchorage	peer *	C_ASSO	see 9.2.6
Fairway	peer *	C_ASSO/C_AGGR	see 10.4
Radar beacon	peer *	C_AGGR	see 12.10
			table 15.1

*	Relationships defined using collection objects are assumed to be peer to peer. The RIND subfield of the collection feature record must be “peer” (see ENC Product Specification, clause 3.9)

**	Such a C_ASSO object must not be used to link the individual elements of the navigation lines and tracks, but should be used to show the relationship between the navigation lines and tracks and the associated dangers.

Relationships may be hierarchical.

If a collection object extends beyond a cell boundary (i.e. the objects that makes up the collection are spread over multiple cells), the collection object should be repeated in each cell that contains one or more component objects. However, only the objects that exist in the cell that contains the instance of the collection object can be referenced by that collection object. If this technique is used, each instance of the original collection object must have the same feature identifier (LNAM). It is up to the application (e.g. the ECDIS) that uses the cells to rebuild the complete collection object based on the unique feature identifier.

It is highly recommended that no use be made of pointers that reference objects outside the cell in which the pointer is encoded. Use of such pointers cannot be prohibited, as no such rule exists in the ENC Product Specification.

__________

Page intentionally left blank
ALPHABETICAL INDEX